## Slide 1: Autonomous Mission Management of Unmanned Vehicles using Soar
Scott Hanford
Penn State Applied Research Lab
Distribution A
Approved for Public Release; distribution is unlimited

## Slide 2: MCM background
UUVs used to automate parts of Mine Countermeasures (MCM) mission
Interest in autonomously altering missions based on sensor data obtained during mission
Goal of our project: collaborate with NSWC-PCD to explore use of cognitive architecture for management of established autonomy capabilities

## Slide 3: Representative MCM autonomy
Task Spooler
Mission Script
Vehicle Controller
Behaviors
Transit
Survey
Loiter
Spiral
…
Launch
Spiral
Transit
Survey
Transit
Loiter at pickup

## Slide 4: Mission Management using Soar
Task Spooler
Mission Script
Behaviors
Vehicle Controller
Transit
Survey
Loiter
Spiral
…
AME
AMR
Soar Mission Manager
Mission Management
Adaptive Mission Execution (AME)
Autonomous Mission Replanning (AMR)
Explanation Facility
Soar interacts with rest of system using ZeroMQ

## Slide 5: Explanation Facility
  Goal is for users (MCM operators & SMEs, not necessarily Soar users) to be able to:
  Understand what decisions Soar agent made
    What pieces of information were used
    Alternatives considered
  Identify undesirable decisions and provide context for agent developer to investigate
This talk
  Mechanisms used to help generate explanations
  Examples of explanations

## Slide 6: Initial explanation
Fault condition: below-max-depth condition recorded.
Operator to manage depth problem proposed to manage-safety-fault based on existence of fault-condition
Elaboration tests that UUV depth is below maximum depth threshold – creates WME indicating fault condition
Sensor input indicates UUV depth (180.56) is below maximum allowable depth
E17
below-max-depth
^fault-condition
^name
O11
manage-safety-fault
below-max-depth
^fault-condition
When operator is applied, an explanation is generated (without details of UUV depth):
Missing what input caused this condition to be recognized

## Slide 7: Storing elaborated information
below-max-depth
E17
^fault-condition
N35
^value
S21
^supporting-wmes
180.0
180.56
^threshold
^measured-value
Operator proposed to manage depth problem has additional attribute to reference specific fault condition triggering proposal
O11
manage-safety-fault
below-max-depth
^name
^fault-condition
N35
^condition-id
Alter elaboration that tests that UUV depth is below maximum depth threshold fault to save additional information

## Slide 8: Generation of explanation
Create explanation object in WM using information from operator attributes
E23
^fault-condition
F38
E1
^explanation
^condition-type
^id
below-max-depth
N35
Use elaboration to copy supporting WMEs from WM object stored in id
180.0
180.56
^threshold
^measured-value
Use another elaboration to generate explanation based on attributes present
Fault condition: below-max-depth condition recorded. UUV depth (180.136) is below maximum depth threshold (180.0).
^string

## Slide 9: Agent-generated explanation
Agent output:
<698.6> Mission status: UUV has started navigation to waypoint 1 of survey behavior.
<736.7> Fault condition: below-max-depth condition recorded. UUV depth (180.10) is below maximum depth threshold (180.).
<736.7> Fault strategy generation: Soar agent generated strategy to resolve below-max-depth condition: UUV commanded to maintain depth (at 175.).
<738.2> Successful fault strategy: strategy to maintain depth (at 175.) has decreased UUV depth (179.97) above maximum depth threshold (180.).
<738.2> Mission status: UUV can not return to behavior's desired control mode, continue using fault strategy to maintain depth (at 175.).
<738.2> Mission strategy: Abandon track number 4 (waypoint 1) because altitude is too high relative to altitude intended for survey.
1
2
3

## Slide 10: Explanation of alternatives
Soar mission manager will ideally have more than one tactically appropriate strategy to consider when a decision is necessary
Want to explain rationale for choosing one strategy over another
  Encode each possible strategy as a Soar operator
  Propose each strategy whenever it is tactically appropriate
  Use operator preference rules to select between multiple tactically appropriate operators based on context
  In RHS of operator comparison rule, add information to preferred operator about the operator it is preferred over

## Slide 11: Alternative strategy explanation
Agent output:
<115.7> Agent has detected that currents are affecting mission progress.
<115.7> Vehicle recorded as being in the volume layer of current when detection that currents are affecting mission progress first occurred.
<115.7> Change depth to 15. meters to attempt to search for more favorable current in surface current layer.
<115.7> Also considered changing altitude to 5. meters to search for more favorable current in bottom, but distance to move in water column to reach bottom (263.6 m) was greater than distance to move to surface layer (85.3 m).
Bottom
Volume
Surface
3 layers of current: surface, volume, bottom
Consider attempting to transit in different layer  prefer closer layer

## Slide 12: Summary
Nuggets
  Have used Soar to increase robustness of representative UUV autonomy by adapting behaviors
  Explanation of decisions useful to understand how agent has applied domain specific knowledge
Coal
  Access to complexity of context to fully demonstrate usefulness of Soar’s capabilities can be challenging
This material is based upon work supported by the Office of Naval Research under grant number N00014-10-G-0259/0031. Any opinions, findings, and conclusions or recommendations expressed are those of the authors and do not necessarily reflect the views of the sponsor.