## Slide 1
Andreas Kosmas Kakolyris
F. Nisa Bostancı
Harsh Songara
Konstantinos Kanellopoulos
Ataberk Olgun
Konstantinos Marios Sgouras
A. Giray Yağlıkçı
İsmail Emir Yüksel
Umut Başer
Onur Mutlu
ColumnKeeper: Efficient Solutions to the ColumnDisturb Vulnerability in DRAM-based Systems
Notes: Hi all, my name is Andreas and today I will be presenting our work titled ColumnKeeper Efficient Solutions to the ColumnDisturb Vulnerability in DRAM-based Systems

## Slide 2: Executive Summary
Problem: DRAM chips are vulnerable to ColumnDisturb, a new, column-based read disturbance phenomenon. Naively mitigating ColumnDisturb incurs significant overheads.
Goal: Design mechanisms that mitigate ColumnDisturb bitflips with low performance, energy and area overheads
Key Idea: Track row activations at subarray granularity. Iteratively refresh all rows.
ColumnKeeper-D (Deterministic): Uses separate activation counters for odd and even bitlines of each subarray and issues a preventive refresh when either counter reaches a predetermined threshold
ColumnKeeper-P (Probabilistic): Probabilistically issues refreshes to one row in three consecutive subarrays upon a row activation in the middle subarray
Evaluation
ColumnKeeper mitigates ColumnDisturb bitflips with low overheads at current (1M) and “near-future” (128K) thresholds
ColumnKeeper can mitigate ColumnDisturb bitflips with low overheads even at low thresholds (16K) with changes to DRAM microarchitecture
https://github.com/CMU-SAFARI/ColumnKeeper
Notes: This is a high-level summary of my talk.
[CLICK] The problem that we tackle is that …
[CLICK] Our goal in this paper is to
[CLICK] To achieve this, our key idea is to
We propose two mechanisms. The first is
[CLICK] ColumnKeeper-D which …
The second is:
ColumnKeeper-P, which
Our evaluation shows that
[CLICK] …
And
[CLICK …]
[CLICK ]ColumnKeeper is open source and available at the link below

## Slide 3: Outline
Background
Motivation
ColumnKeeper-D (Deterministic)
Evaluation
Conclusion
ColumnKeeper-P (Probabilistic)
Notes: This is the outline of my talk.

## Slide 4: Outline
Background
Motivation
ColumnKeeper-D (Deterministic)
Evaluation
Conclusion
ColumnKeeper-P (Probabilistic)
Notes: I’ll start with a bit of background

## Slide 5: DRAM Organization
CPU
DRAM Module
DRAM Chip
DRAM
Channel
Notes: This is a high-level view of a modern system where a CPU and a DRAM module communicate over a DRAM Channel.
[CLICK] The DRAM module is comprised of multiple DRAM chips.

## Slide 6: DRAM Organization
wordline
bitline
DRAM Cell
capacitor
DRAM Subarrays
…
…
SA
SA
SA
SA
SA
SA
DRAM
Chip
DRAM Column
…
…
DRAM Chip
Chip I/O
Bank
Bank
Bank
Bank
Bank
Bank
DRAM Bank
DRAM Subarray 0
Sense Amplifiers
DRAM Subarray 1
Sense Amplifiers
DRAM Subarray 2
Sense Amplifiers
DRAM Subarray N
Sense Amplifiers
…
DRAM Row
Notes: [CLICKx2] The DRAM chip is comprised of multiple DRAM banks.
[CLICK] Each bank is composed of multiple subarrays and sense amplifiers and
[CLICK] within each subarray, there is a two dimensional array of DRAM cells
[CLICK] The cells are organized into rows that are selected using wordlines
[CLICK] and columns that connect the dram cells to the sense amplifiers via bitlines

## Slide 7: DRAM Organization
SA
SA
SA
SA
1
0
1
1
1
0
1
1
ACTIVATE: Fetch the row into the sense amplifiers
1
READ/WRITE: Retrieve or
update data
2
PRECHARGE: Prepare the bank for a new ACTIVATE
3
to/from I/O
Notes: To access DRAM one must first
[CLICK] Activate (also known as opening) a DRAM row which latches its data into the row buffer
[CLICK] And then retrieve or update data with a READ or WRITE command
[CLICK] To access data in a different row the DRAM bank must be precharged (also known as closing a row) which prepares it for a new ACTIVATE command

## Slide 8: DRAM Read Disturbance: RowHammer
SA
SA
SA
SA
Read disturbance in DRAM breaks memory isolation
Prominent example: RowHammer
Victim Row
Victim Row
Aggressor Row
Notes: Repeatedly opening and closing rows may cause read disturbance phenomena, which break memory isolation
One prominent example is RowHammer.
[CLICK] This is a picture of a DRAM bank
[CLICK] To induce RowHammer bitflips, we repeatedly open and close a DRAM row called an aggressor row
[CLICK] Too many activations cause bitflips in adjacent rows in the same subarray. Rows that experience bitflips are called victim rows

## Slide 9: DRAM Read Disturbance: RowHammer
SA
SA
SA
SA
Read disturbance in DRAM breaks memory isolation
Prominent example: RowHammer
Victim Row
Victim Row
Aggressor Row
RowHammer causes bitflips in adjacent rows in the same subarray
Notes: The key point here is that RowHammer causes bitflips in adjacent rows in the same subarray

## Slide 10: DRAM Read Disturbance: RowPress
SA
SA
SA
SA
Read disturbance in DRAM breaks memory isolation
Another prominent example: RowPress
Victim Row
Victim Row
Aggressor Row
keep open
Notes: Another Read Disturbance phenomenon, RowPress, induces bitflips by
[CLICK ] keeping rows open for long periods of time.

## Slide 11: DRAM Read Disturbance: RowPress
SA
SA
SA
SA
Read disturbance in DRAM breaks memory isolation
Another prominent example: RowPress
Victim Row
Victim Row
Aggressor Row
RowPress causes more bitflips in adjacent rows in the same subarray
keep open
Notes: Doing so causes even more bitflips in adjacent rows

## Slide 12: DRAM Read Disturbance: ColumnDisturb
ColumnDisturb: Repeatedly hammering or pressing a DRAM row disturbs many DRAM cells on the same DRAM column
Subarray
Subarray
Subarray
SA
SA
SA
SA
Open-bitline architecture: columns of a single row span multiple subarrays
Notes: ColumnDisturb is a new and fundamentally different DRAM read disturbance phenomenon.
[CLICK] Repeatedly hammering or pressing a DRAM row disturbs many DRAM cells on the same DRAM column
[CLICK] Due to modern DRAM’s open-bitline architecture the columns span multiple subarrays

## Slide 13: DRAM Read Disturbance: ColumnDisturb
ColumnDisturb: Repeatedly hammering or pressing a DRAM row disturbs many DRAM cells on the same DRAM column
Subarray
Subarray
Subarray
All cells
Cells on odd columns
Cells on even columns
Notes: ColumnDisturb affects all cells in the hammered subarray
[CLICK] But only cells in either the odd or the even columns in neighboring subarrays

## Slide 14: DRAM Read Disturbance: ColumnDisturb
ColumnDisturb: Repeatedly hammering or pressing a DRAM row disturbs many DRAM cells on the same DRAM column
Subarray
Subarray
Subarray
All cells
Cells on odd columns
Cells on even columns
ColumnDisturb affects DRAM cells across
three consecutive DRAM subarrays (up to 3072 DRAM rows)
ColumnDisturb induces bitflips within the DDR4 refresh window
The number of activations required to induce ColumnDisturb bitflips (NCD) is currently 1M
Scaling studies show ColumnDisturb is getting worse in newer chips
Notes: [CLICK] ColumnDisturb affects DRAM cells across three consecutive DRAM subarrays which is up to 3K rows
[CLICK] And it has been shown to induce bitflips within the DDR4 refresh window
[CLICK] The number of activations required to induce ColumnDisturb bitflips or N_CD is currently 1M
[CLICK] and scaling studies show that column disturb is getting worse in newer chips

## Slide 15: Outline
Background
Motivation
ColumnKeeper-D (Deterministic)
Evaluation
Conclusion
ColumnKeeper-P (Probabilistic)
Notes: Let me motivate the problem a bit more

## Slide 16: Mitigating ColumnDisturb (I)
The easiest way of mitigating ColumnDisturb is to reduce the DRAM refresh window so that all rows are refreshed before bitflips can occur
Significant performance overheads at near-future ColumnDisturb thresholds:
More than 50% for workloads with high memory intensity
Significant DRAM energy overheads at near-future ColumnDisturb thresholds:
More than 6x increase in energy consumption
Mitigating ColumnDisturb by increasing the DRAM refresh rate
incurs prohibitive overheads
Notes: The easiest way of mitigating ColumnDisturb is to reduce the DRAM refresh window so that all rows are refreshed before bitflips can occur
However this comes at:
[CLICK] Significant performance overheads at what we consider near-future ColumnDisturb thresholds of 128K activations. For example we see a more than 50% drop in performance for workloads with high memory intensity.
[CLICK] We also see a more than 6x increase in DRAM energy consumption for the same workloads and thresholds
[CLICK] Overall, mitigating ColumnDisturb by increasing the DRAM refresh rate incurs prohibitive overheads

## Slide 17: Mitigating ColumnDisturb (II)
Alternative method: Modifying RowHammer mitigation mechanisms to protect against ColumnDisturb
RowHammer mitigations such as Per-Row Activation Counting (PRAC):
Track activations at the row granularity
Only refresh a few neighboring victim rows
Using PRAC to mitigate ColumnDisturb requires:
Aggressively configuring PRAC to fire at a low threshold
Refreshing all 3072 rows across three subarrays
Modified PRAC incurs prohibitive overheads
Notes: An alternative method one would think of would be to modify existing RowHammer mitigation mechanisms to protect agains ColumnDisturb
[CLICK] However, RowHammer mitigation mechanisms such as Per-Row Activation Counting or PRAC track activations at the row granularity and only refresh a few neighboring victim rows
[CLICK] Using PRAC to mitigate ColumnDisturb requires aggressively configuring PRAC to fire at a low threshold and then refreshing all 3072 rows across three subarrays
[CLICK] As a result using a modified PRAC mitigation to protect against ColumnDIsturb also incurs prohibitive overheads.

## Slide 18: Our Goal
Design mechanisms
that prevent ColumnDisturb bitflips
at low performance, energy, and area overheads
Notes: Our Goal in this work is to:

## Slide 19: Our Overarching Key Idea
Track activations at subarray granularity
Iteratively refresh all rows within each subarray
Notes: Our overarching key idea is to track activations at the subarray granularity and
Iteratively refresh all rows within each affected subarray

## Slide 20: Outline
Background
Motivation
ColumnKeeper-D (Deterministic)
Evaluation
Conclusion
ColumnKeeper-P (Probabilistic)
Notes: We propose two mechanisms, the first of which, ColumnKeeper-D uses

## Slide 21: Key Observation
Activations in one subarray affect all columns in that subarray but
either odd or even columns in neighboring subarrays
Notes: The key observation that …

## Slide 22: Key Observation
SA
SA
SA
SA
Subarray A
Subarray B
Subarray C
Χ
Υ
Nodd = Χ
Neven = Χ
Nodd = Υ
Neven = Χ
Nodd = Υ
Neven = Υ
Total ACTs = Χ
Actual ACTs = Χ
Total ACTs = Υ
Actual ACTs = Υ
Total ACTs = Χ+Υ
Actual ACTs = max{Χ,Υ}
SA
SA
SA
SA
Activations in one subarray affect all columns in that subarray but
either odd or even columns in neighboring subarrays
Notes: Here is a picture of three consecutive subarrays A, B and C in a DRAM bank.
[CLICK] We hammer a row in subarray A X times [CLICK]
[CLICK] And we hammer a rows in subarray C Y times [CLICK]
As a result:
[CLICK ]The number of hammers in both the odd and even columns of subarray A is X.
[CLICK] The number of hammers both in the odd and even columns of subarray C is Y.
However,
[CLICK] in the middle subarray B, these differ, with Y hammers in the odd columns and X hammers in even columns.
The actual number of activations affecting the cells of A and C matches the total number of activations affecting the cells in those subarrays
[CLICK] However, in subarray B the total number of acts in the subarray is X+Y while the actual hammer count affecting any single cell in the subarray is the maximum of X and Y

## Slide 23: Key Observation
Activations in one subarray affect all columns in that subarray but
either odd or even columns in neighboring subarrays
Υ
Χ
SA
SA
SA
SA
Subarray A
Subarray B
Subarray C
Nodd = Χ
Neven = Χ
Nodd = Υ
Neven = Χ
Nodd = Υ
Neven = Υ
Total ACTs = Χ
Actual ACTs = Χ
Total ACTs = Υ
Actual ACTs = Υ
Total ACTs = Χ+Υ
Actual ACTs = max{Χ,Υ}
SA
SA
SA
SA
In the worst case when Χ = Υ Total ACTs = 2 Actual ACTs
Naively counting the activations affecting a subarray overestimates the activation count of cells and increases overheads
Notes: In the worst case were X = Y
the total number of activations affecting the middle subarray can be two times the actual number of activations affecting any cell in that subarray

## Slide 24: ColumnKeeper-D Key Idea
Separately count activations in odd and even columns of each subarray to mitigate ColumnDisturb at low performance and energy overheads
Notes: To solve this is ColumnKeeper-D’s key idea is to:

## Slide 25: ColumnKeeper-D Overview
Memory Request Scheduler
5
8
4
…
CT-Even
ColumnKeeper-D consists of:
Counter Table – Even (CT-Even): Counts activations in even columns
Counter Table – Odd (CT-Odd): Counts activations in odd columns
Row Pointer Table (RPT): Points to the next row to be preventively refreshed in each subarray
3
2
9
…
CT-Odd
NSUBARRAYS
RPT
…
Notes: Here is an overview of ColumnKeeper-D.
ColumnKeeper-D consists of:
[CLICK] Counter Table – Even or CTE , which counts activations in the even columns of a subarray,
[CLICK] Counter Table – Odd or CTO, which counts activations in the odd columns of a subarray, and
[CLICK] the Row Pointer Table or RPT which always points to the next row to be preventively refreshed in each subarray
[CLICK] Let’s assume CTE and CTO contain some values
Do CT-Even and CT-Odd

## Slide 26: ColumnKeeper-D Overview
RPT
…
Memory Request Scheduler
5
8
4
…
CT-Even
Upon a row activation in subarray k, ColumnKeeper-D:
Increments both the CT-Even and CT-Odd entries for subarray k
Increments the CT-Even entry for the previous subarray
Increments the CT-Odd entry for the next subarray
3
2
9
…
CT-Odd
NSUBARRAYS
8
2
+1
+1
5
+1
9
+1
9
3
6
10
Notes: When a row activation happens in a subarray k, ColumnKeeper-D:
[CLICK] increments both the CTE and CTO entries in subarray k but
[CLICK] increments only the CTE entry for the previous subarray
[CLICK] and the CTO entry in the next subarray
[CLICKx2]

## Slide 27: ColumnKeeper-D Overview
RPT
…
Memory Request Scheduler
NSUBARRAYS
4
…
CT-Even
3
…
CT-Odd
9
3
6
10
MAX
MAX
MAX
10
9
6
Upon a row activation in subarray k, ColumnKeeper-D:
Calculates the maximum value of the two counters for the three subarrays
Compares the calculated value to a predetermined threshold (NPR)
NPR = 10
Notes: [CLICK] It then calculates the maximum value of the two counters in each of the three subarrays
[CLICK] and Compares the calculated value to a predetermined threshold which we call N_PR

## Slide 28: ColumnKeeper-D Overview
RPT
…
Memory Request Scheduler
NSUBARRAYS
4
…
CT-Even
3
…
CT-Odd
9
3
6
10
MAX
MAX
MAX
10
9
6
Row activation in subarray k:
Calculates the maximum value of the two counters for the three subarrays
Compares the calculated value to a predetermined threshold (NPR)
NPR = 10
We set NPR to NCD divided by the subarray size
This ensures all rows are iteratively refreshed before reaching NCD
Notes: [CLICK] we set N_PR to the column disturb threshold NCD divided by the subarray size .
[CLICK] This ensures all rows are iteratively refreshed before reaching NCD.

## Slide 29: ColumnKeeper-D Overview
RPT
…
Memory Request Scheduler
NSUBARRAYS
4
…
CT-Even
3
…
CT-Odd
9
3
6
10
MAX
MAX
MAX
10
9
6
Row activation in subarray k:
Calculates the maximum value of the two counters for the three subarrays
Compares the calculated value to a predetermined threshold (NPR)
If the maximum counter value for a subarray exceeds NPR ColumnKeeper-D decides to issue a preventive refresh for that subarray
NPR = 10
Y
N
N
Notes: If the maximum counter value for a subarray exceeds NPR

## Slide 30: ColumnKeeper-D Overview
RPT
…
Memory Request Scheduler
NSUBARRAYS
4
…
CT-Even
3
…
CT-Odd
9
3
6
10
MAX
MAX
MAX
10
9
6
ColumnKeeper-D:
Issues an ACT command followed by a PRE command to the Row Address pointed by the corresponding RPT entry
Increments the RPT entry to point to the next row in that subarray
Zeroes the CT-Even and CT-Odd entries for that subarray
NPR = 10
Y
N
N
Preventive Refresh
ACT+PRE
Row Address
6
+1
7
0
0
Notes: To do this it issues an ACT command followed by a PRE command to the Row Address pointed by the corresponding RPT entry.
[CLICK] it then increments the RPT entry to point to the next row in that subarray and finally
[CLICK] it zeroes the CTE and CTO entries for that subarray, restarting the counting process

## Slide 31: Outline
Background
Motivation
ColumnKeeper-D (Deterministic)
Evaluation
Conclusion
ColumnKeeper-P (Probabilistic)
Notes: We also propose a probabilistic variant of our ColumnKeeper mechanism called ColumnKeeper-P

## Slide 32: ColumnKeeper-P Key Idea
Probabilistically issue preventive refreshes to avoid activation counting and mitigate ColumnDisturb at lower area overhead
Notes: The key idea of ColumnKeeper is to:

## Slide 33: ColumnKeeper-P Overview
RPT
…
Memory Request Scheduler
NSUBARRAYS
ColumnKeeper-P substitutes ColumnKeeper-D’s deterministic activation counting mechanism with a probabilistic one
Row Address
6
+1
7
4
…
CT-Even
3
…
CT-Odd
9
3
6
10
MAX
MAX
MAX
10
9
6
NPR = 10
Y
N
N
0
0
Preventive Refresh
ACT+PRE
Notes: ColumnKeeper-P substitutes …

## Slide 34: ColumnKeeper-P Overview
RPT
…
Memory Request Scheduler
Upon a row activation in one subarray:
ColumnKeeper-P flips a coin that lands heads up with a predetermined probability (PPR)
Coin Flip w/ Probability PPR
Notes: Upon a row activation in one subarray:
[CLICK] ColumnKeeper-P flips a coin that lands heads-up with a predetermined probability P_PR
Change coin

## Slide 35: ColumnKeeper-P Overview
RPT
…
Memory Request Scheduler
Upon a row activation in one subarray:
ColumnKeeper-P flips a coin that lands heads up with a predetermined probability (PPR)
Preventive Refreshes
ACT+PRE
$
Coin Flip w/ Probability PPR
PPR is calculated to upper bound the probability of a ColumnDisturb bitflip occurring during a year of continuous ColumnDisturb attack
Notes: [CLICK] P_PR is calculated to …

## Slide 36: ColumnKeeper-P Overview
RPT
…
Memory Request Scheduler
Upon a row activation in one subarray:
ColumnKeeper-P flips a coin that lands heads up with a predetermined probability (PPR)
If the coin lands heads up, ColumnKeeper-P issues preventive refreshes for that subarray and its neighbors and increments all three RPT entries
Preventive Refreshes
ACT+PRE
2
7
9
2
7
9
+1
+1
+1
Y
Row Addresses
Heads up?
Coin Flip w/ Probability PPR
Notes: If the coin lands heads up, ColumnKeeper-P issues prefentive refreshes for that subarray and its neighbors and [CLICK] increments all three RPT entries

## Slide 37: More Details in the Paper
Detailed calculation of NPR for ColumnKeeper-D
Security analysis of ColumnKeeper-D
Detailed calculation of PPR for ColumnKeeper-P
Monte-Carlo security analysis of ColumnKeeper-P
Notes: We have a lot more details in the paper such as
[CLICK] Detailed calculation of NPR for ColumnKeeper-D
[CLICK]Security analysis of ColumnKeeper-D
[CLICK] Detailed calculation of PPR for ColumnKeeper-P
[CLICK] Monte-Carlo security analysis of ColumnKeeper-P
Extend terminology

## Slide 38: Outline
Background
Motivation
ColumnKeeper-D (Deterministic)
Evaluation
Conclusion
ColumnKeeper-P (Probabilistic)
Notes: I will now move to the evaluation section

## Slide 39: Methodology
Performance and energy consumption evaluation: cycle-level simulations using Ramulator2 [Luo+, CAL 2023] and DRAMPower [Chandrasekar+, DATE 2013]
System Configuration:
  Processor 1 or 4 cores, Last-Level Cache: 2 MiB/core
  DRAM 16GB DDR4, 1 channel, 2 rank/channel, 4 bank groups,
  4 banks/bank group, 64K rows/bank, 1K rows/subarray
  Mem. Ctrl. 64-entry read/write request queue,
  Scheduling policy: FR-FCFS, Open-Row Policy
  Address mapping: RoBaRaCoCh
  ColumnKeeper-D (Det) or ColumnKeeper-P w/ yearly failure probability of 10-3 (Pr-Perf) or 10-12 (Pr-Cons)
Workloads:
62 single-core workloads from SPEC CPU2006, SPEC CPU2017, TPC, MediaBench, and YCSB categorized by Row Buffer Misses per-kilo-instructions (RBMPKI)
60 quad-core workload mixes synthesized from the resulting RBMPKI categories
Notes: [CLICK] We evaluate ColumnKeeper using Ramulator2 integrated with DRAM power
[CLICK] This is the configuration of our system with 1 or 4 cores and 16GB of DDR4 memory
[CLICK] We evaluate ColumnKeeper-D or CKD for short and
ColumnKeeper-P configured for a yearly failure probability of 10 to the minus three and 10 to the minus 12 which we call CKP3 and CKP12, respectively.
[CLICK] We evaluate 62 single-core workloads from a variety of benchmark suites categorized by RowBuffer misses per Kilo instructions and
60 quad-core workload mixes from the result RBMPKI categories
Aggressively Optimize Legends

## Slide 40: Evaluation: Single-Core Performance
Notes: Let's start by evaluating single-core performance [CLICK ]

## Slide 41: Evaluation: Single-Core Performance
Higher is better
More memory-intensive
Notes: Let's start by evaluating single-core performance [CLICK ]
[CLICK] Here, the y-axis shows IPC normalized to the baseline system with no ColumnDisturb mitigation
[CLICK] the x-axis shows workloads organized by increasing RBMPKI which corresponds to more memory-intensive workloads.
[CLICK] For each RBMPKI category, different colored boxplots correspond to different ColumnKeeper mechanisms, with pink for CKD, blue for CKP3 and red for CKP12

## Slide 42: Evaluation: Single-Core Performance
ColumnKeeper-D and –P incur low (<1%) average performance overheads for current ColumnDisturb thresholds (1M)
Notes: We observe that ColumnKeeper-D and ColumnKeeper-P incur low, that is under 1% average performance overheads for the current column disturb threshold of 1M

## Slide 43: Evaluation: Single-Core Performance
Notes: We repeat the same experiment for ColumnDisturb thresholds of 128K and 16K and we see that

## Slide 44: Evaluation: Single-Core Performance
Performance overheads increase for more memory-intensive workloads
Notes: [CLICK] For all thresholds, our performance overheads increase for more memory intensive workloads.

## Slide 45: Evaluation: Single-Core Performance
Performance overheads increase for more memory-intensive workloads
All ColumnKeeper mechanisms incur significant performance overheads at low ColumnDisturb thresholds of NCD=16K
Notes: [CLICK] We also see that all ColumnKeeper mechanisms incur …
Give example
3x Thin banners

## Slide 46: Evaluation: DRAM Energy (Single-Core)
Notes: This is our evaluation of ColumnKeeper’s impact on DRAM energy consumption for single-core workloads.

## Slide 47: Evaluation: DRAM Energy (Single-Core)
Lower is better
More memory-intensive
Notes: [CLICK] The y-axis shows DRAM energy consumption normalized to a system with no ColumnDisturb mitigation. Here, lower is better
[CLICK] Again, the x-axis is sorted in order of increasing memory-intensity

## Slide 48: Evaluation: DRAM Energy (Single-Core)
Energy overheads increase for more memory-intensive workloads
Low energy overheads for current thresholds
Significant energy overheads for future low thresholds
Notes: Our DRAM energy results largely mimic those for performance. Specifically, we see that
[CLICK] The energy overheads increase for more memory-intensive workloads and
[CLICK] that we have low energy overheads for current thresholds but
[CLICK] but significant energy overheads for future lower thresholds.

## Slide 49: Evaluation: Multi-Core Performance
Notes: Let’s move on to multi-core evaluation. [CLICK]
These are our results. [CLICK]
[CLICK] The Y axis shows weighted speedup normalized to the same system with no ColumnDisturb mitigation
[CLICK] The X axis shows different workloads mixes, organized from left to right by increasing memory intensity
[CLICK] Different colored boxplots correspond to different mechanisms.

## Slide 50: Evaluation: Multi-Core Performance
Higher is better
More memory-intensive
Notes: [CLICK] The Y axis shows weighted speedup normalized to the same system with no ColumnDisturb mitigation
[CLICK] The X axis shows different workloads mixes, organized from left to right by increasing memory intensity
[CLICK] Different colored boxplots correspond to different mechanisms.

## Slide 51: Evaluation: Multi-Core Performance

## Slide 52: Evaluation: Multi-Core Performance
Performance overheads increase for memory-intensive workload mixes
Low performance overheads for current thresholds
Significant performance overheads for future low thresholds

## Slide 53: Evaluation: Multi-Core Performance
1.5%
More pronounced difference between CK-D an CK-P than single-core

## Slide 54: Evaluation: Sensitivity to Subarray Size
Notes: Το ColumnKeeper’s overheads we examine its sensitivity to the subarray size:
[CLICK] Here the x-axis shows the size of the subarray in terms of number of rows
[CLICK] The y axis shows IPC normalized to a baseline system with a subarray size of 1024 rows and no ColumnDisturb mitigation
[CLICK] Different colored boxplots correspond to different mechanisms.
[CLICK] These are our results and we observe that
[CLICK] Smaller subarrays, for example 128 rows, eliminate the overheads.

## Slide 55: Evaluation: Sensitivity to Subarray Size
Higher is better
Smaller Subarrays
Notes: Το ColumnKeeper’s overheads we examine its sensitivity to the subarray size:
[CLICK] Here the x-axis shows the size of the subarray in terms of number of rows
[CLICK] The y axis shows IPC normalized to a baseline system with a subarray size of 1024 rows and no ColumnDisturb mitigation
[CLICK] Different colored boxplots correspond to different mechanisms.
[CLICK] These are our results and we observe that
[CLICK] Smaller subarrays, for example 128 rows, eliminate the overheads.

## Slide 56: Evaluation: Sensitivity to Subarray Size
Smaller subarrays (128 rows) eliminate the overheads of ColumnKeeper
for current ColumnDisturb thresholds (1M)
Notes: Το ColumnKeeper’s overheads we examine its sensitivity to the subarray size:
[CLICK] Here the x-axis shows the size of the subarray in terms of number of rows
[CLICK] The y axis shows IPC normalized to a baseline system with a subarray size of 1024 rows and no ColumnDisturb mitigation
[CLICK] Different colored boxplots correspond to different mechanisms.
[CLICK] These are our results and we observe that
[CLICK] Smaller subarrays, for example 128 rows, eliminate the overheads.

## Slide 57: Evaluation: Sensitivity to Subarray Size
Smaller subarrays reduce the overheads of ColumnKeeper
for all ColumnDisturb thresholds
Notes: This applies in general for all the thresholds we evaluate

## Slide 58: Evaluation: Sensitivity to Subarray Size
Notes: Smaller subarrays significantly reduce the overheads of ColumnKeeper even at very low overheads

## Slide 59: Evaluation: Sensitivity to Subarray Size
Smaller subarrays reduce the overheads of ColumnKeeper
even at very low thresholds
Notes: []
Smaller subarrays significantly reduce the overheads of ColumnKeeper even at very low overheads

## Slide 60: Evaluation: Area and Power Overheads
ColumnKeeper requires:
7.5 KB of SRAM for ColumnKeeper-D
2.5 KB of SRAM for ColumnKeeper-P
Hardware Implementation & Synthesis:
ColumnKeeper implemented in Verilog
OpenRoad + NanGate 45nm Open-Source Cell Library
Area Overheads:
0.1 mm2 for ColumnKeeper-D
0.03 mm2 for ColumnKeeper-P
Power Overheads:
50 mW for ColumnKeeper-D
15 mW for ColumnKeeper-P
Notes: Implementing ColumnKeeper requires:
[CLICK]
[CLICK]
We implement

## Slide 61: More in the Paper
Evaluation of ColumnKeeper with Subarray-level Parallelism [Kim+, ISCA 2012]
Impact of physical page allocation policy on the performance overheads of ColumnKeeper
Performance evaluation of ColumnKeeper integrated with RowHammer mitigation mechanisms
Performance evaluation under adversarial workloads
An in-DRAM implementation of our design
Notes: Color

## Slide 62: Available on arXiv
https://arxiv.org/pdf/2606.22632

## Slide 63: Artifact Evaluated & Open-Source
https://github.com/CMU-SAFARI/ColumnKeeper

## Slide 64: Outline
Background
Motivation
ColumnKeeper-D (Deterministic)
Evaluation
Conclusion
ColumnKeeper-P (Probabilistic)
Notes: This is the outline of my talk

## Slide 65: Conclusion
Key Idea: Track row activations at subarray granularity and iteratively refresh all affected rows in a subarray
Goal: Mitigate ColumnDisturb bitflips at low overhead
Key Results:
ColumnKeeper prevents ColumnDisturb bitflips with low overheads for current and near-future thresholds
ColumnKeeper can prevent ColumnDisturb bitflips at low overheads for low thresholds with changes to DRAM microarchitecture
ColumnKeeper-D: Uses separate activation counters for odd and even columns of each subarray
ColumnKeeper-P: Probabilistically issues refreshes to one row in three consecutive subarrays upon a row activation in the middle subarray

## Slide 66
ColumnKeeper: Efficient Solutions to the ColumnDisturb Vulnerability in DRAM-based Systems
Paper
Code

## Slide 67
ColumnKeeper: Efficient Solutions to the ColumnDisturb Vulnerability in DRAM-based Systems
F. Nisa Bostancı
Harsh Songara
Konstantinos Kanellopoulos
Ataberk Olgun
Konstantinos Marios Sgouras
A. Giray Yağlıkçı
İsmail Emir Yüksel
Umut Başer
Onur Mutlu
Andreas Kosmas Kakolyris
Backup Slides

## Slide 68: Evaluation: Detailed Single-Core Results

## Slide 69: Evaluation: Sensitivity to Page Allocation
No significant difference in performance between the two allocators

## Slide 70: Evaluation: In-DRAM Implementation
The in-DRAM implementation of ColumnKeeper-D reduces its overheads at low ColumnDisturb thresholds

## Slide 71: ColumnKeeper-P: PPR Calculation
Methodology
Similar to the one proposed in HiRA [Yaglikci+, MICRO 2022]
Considers the maximum number of attacks that can happen in a refresh window
At least one of these attacks has to succeed
To induce bitflips: The number of preventive issues issued to a subarray must be lower than the subarray size (S) when the ColumnDisturb threshold is reached
Total number of preventive refreshes issued after N activations (MN):
Sum of Bernoulli random variables
MN follows a binomial distribution

## Slide 72: ColumnKeeper-P: PPR Calculation
We substitute:
A single ColumnDisturb attack succeeds with probability P1:
Probability of a successful attack within a refresh window based on maximum number of attacks:
Probability of a successful attack within a year (PY):

## Slide 73: ColumnKeeper-P Configuration
Small increases in PPR significantly increase security for the same NCD

## Slide 74: ColumnKeeper-P: Monte-Carlo Simulation
Lower PY leads to more preventive refreshes and a lower HCmax

## Slide 75: Evaluation: Integration w/ RH Mitigations
ColumnKeeper issues ACT+PRE commands:
ACTs and PREs are transparent to RowHammer mitigation mechanisms
RowHammer mitigation mechanisms issue:
ACT + PRE commands
RFM commands
ColumnKeeper operates transparently to RowHammer mitigation mechanisms
RowHammer mitigation mechanisms operate transparently to ColumnKeeper
RFM commands accounted by incrementing all activation counters in affected banks

## Slide 76: Evaluation: Integration w/ RH Mitigations
No destructive interference between RowHammer mitigation mechanisms and ColumnKeeper
NCD = 128K, NRH = 128

## Slide 77: ColumnDisturb: Newer Chips are More Vulnerable
5.1x
1.3x
3x
2.5x
Newer chips tend to be more vulnerable to ColumnDisturb bitflips
This trend is consistent across all tested manufacturers

## Slide 78: Evaluation: Adversarial Workloads
Low performance overheads for current and near-future thresholds
Significant performance overheads for future low thresholds
Notes: We hammer rows across three consecutive subarrays
Normalize to the same workload with no CD mitigation