## Slide 1
COMPOSITE MATERIALS
Material Selection in Design Engineering
Advanced Materials for Modern Engineering Applications

## Slide 2
What are Composite Materials?
Definition: A composite material is a combination of two or more distinct materials with significantly different physical or chemical properties that remain separate and distinct within the finished structure.
Key Components:
Matrix
Continuous phase that binds and protects reinforcement
Reinforcement
Discontinuous phase providing strength and stiffness
Interface
Critical region enabling load transfer between phases

## Slide 3
Why Use Composite Materials?
Superior Strength-to-Weight Ratio
Lighter than metals with comparable or better strength
Design Flexibility
Can be tailored for specific directional properties
Corrosion Resistance
Excellent durability in harsh environments
Fatigue Resistance
Better performance under cyclic loading
Thermal Properties
Low thermal expansion and good insulation
Tailored Performance
Properties optimized for specific applications

## Slide 4
CLASSIFICATION OF COMPOSITES
Understanding the different types and categories

## Slide 5
Matrix Materials
Polymer Matrix
(PMC)
Epoxy
Polyester
Vinyl ester
Thermoplastics
Most common
Easy processing
Metal Matrix
(MMC)
Aluminum
Titanium
Magnesium
Copper
High temperature
Better conductivity
Ceramic Matrix
(CMC)
Silicon carbide
Aluminum oxide
Carbon
Glass ceramics
Ultra-high temp
Wear resistant

## Slide 6
Reinforcement Materials
Carbon Fiber
Highest strength & stiffness, Low density, Expensive
Glass Fiber
Good strength, Low cost, Most common
Aramid Fiber (Kevlar)
High impact resistance, Good tensile strength
Boron Fiber
Very high stiffness, Excellent compression
Ceramic Fibers
High temperature stability, Wear resistance
Natural Fibers
Sustainable, Low cost, Moderate properties

## Slide 7
Carbon Fiber Reinforced Polymers (CFRP)
Properties
Tensile strength: 3-7 GPa
Young's modulus: 200-900 GPa
Density: ~1.6 g/cm³
Superior fatigue properties
Excellent corrosion resistance
Low thermal expansion
Electrically conductive
Applications
Aerospace structures
Automotive components
Sports equipment
Wind turbine blades
Marine vessels
Medical devices
High-end bicycles

## Slide 8
Glass Fiber Reinforced Polymers (GFRP)
Key Characteristics
Lower cost compared to carbon fiber
Good mechanical properties
Excellent electrical insulation
Corrosion resistant
Higher density than carbon fiber
Common Applications
Boat hulls and marine applications
Storage tanks and pipes
Automotive body panels
Building construction materials
Electrical insulation components

## Slide 9
Aramid Fiber Composites (Kevlar)
Unique Properties
Exceptional impact resistance
High tensile strength
Low density (1.44 g/cm³)
Good thermal stability
Vibration damping
Limitations
Poor compression strength
Difficult to machine
UV degradation
Moisture absorption
Higher cost
Applications
Ballistic protection
Pressure vessels
Aerospace components
Sporting goods
Cable reinforcement

## Slide 10
FIBER ORIENTATION & ARCHITECTURE
How fibers are arranged affects composite performance

## Slide 11
Fiber Arrangements
Continuous Unidirectional
Maximum strength in fiber direction
Highly directional loads
Woven Fabric
Balanced properties in two directions
General structural applications
Random Mat
Isotropic in-plane properties
Non-critical structural parts
Braided
Good damage tolerance
Complex shapes, tubes
Multi-directional Layup
Tailored for specific load paths
Aerospace, high-performance

## Slide 12
Manufacturing Processes
Hand Layup
Manual fiber placement, low cost, labor intensive
Spray Layup
Chopped fibers sprayed with resin, fast for large areas
Vacuum Bagging
Atmospheric pressure consolidation, improved quality
Resin Transfer Molding (RTM)
Resin injected into closed mold, good surface finish
Autoclave Curing
High pressure/temperature, aerospace quality
Filament Winding
Automated fiber wrapping, ideal for cylindrical parts
Pultrusion
Continuous process for constant cross-section profiles

## Slide 13
Mechanical Properties of Composites
Property | Carbon/Epoxy | Glass/Epoxy | Kevlar/Epoxy
Density (g/cm³) | 1.55-1.60 | 1.90-2.10 | 1.38-1.40
Tensile Strength (MPa) | 600-1000 | 440-1750 | 1400-2800
Tensile Modulus (GPa) | 120-150 | 38-45 | 70-80
Compression Strength (MPa) | 570-740 | 425-850 | 280-340
Cost Relative | High | Low | Medium-High

## Slide 14
Design Considerations
Load Path Analysis
  Orient fibers along primary load directions for maximum efficiency
Fiber Volume Fraction
  Typically, 50-70% for optimal strength and stiffness
Stacking Sequence
  Layer orientation affects bending, torsion, and coupling effects
Failure Modes
  Consider fiber breakage, matrix cracking, delamination, and debonding
Environmental Factors
  Temperature, moisture, UV exposure affect long-term performance

## Slide 15
Advantages of Composite Materials
✓
Outstanding strength-to-weight ratio
✓
Tailorable mechanical properties
✓
Excellent fatigue and corrosion resistance
✓
Design flexibility for complex shapes
✓
Low thermal expansion coefficient
✓
Reduced assembly requirements
✓
Improved damage tolerance
✓
Electromagnetic transparency (for certain types)

## Slide 16
Limitations & Challenges
High Material Cost
Carbon fiber significantly more expensive than metals
Manufacturing Complexity
Requires specialized processes and skilled labor
Quality Control
Defects (voids, wrinkles) can severely reduce strength
Repair Difficulty
Damage assessment and repair more complex than metals
Recyclability
Thermoset composites difficult to recycle effectively
Property Variability
Anisotropic behavior requires careful analysis
Temperature Limitations
Polymer matrix degrades at elevated temperatures

## Slide 17
Aerospace Applications
Composites now comprise 50%+ of modern aircraft structures by weight
▪ Primary wing and tail structures
▪ Fuselage skin panels
▪ Control surfaces (ailerons, rudders)
▪ Engine nacelles and fairings
▪ Interior components and seating
▪ Landing gear doors
▪ Rotor blades (helicopters)

## Slide 18
Automotive Applications
Body Structures
Hood and roof panels
Fenders and door skins
Chassis components
Bumper beams
Performance Parts
Drive shafts
Suspension arms
Brake discs
Wheels
Benefits
Weight reduction 20-60%
Improved fuel efficiency
Enhanced crashworthiness
Design freedom

## Slide 19
Marine & Sports Applications
Marine Industry
Boat hulls and decks
Yacht masts and spars
Submarine structures
Offshore platforms
Propeller blades
Benefits: Corrosion resistance, reduced weight, lower maintenance
Sports Equipment
Tennis rackets
Golf clubs and shafts
Bicycles and frames
Skis and snowboards
Fishing rods
Benefits: Maximum performance, lightweight, enhanced durability

## Slide 20
Infrastructure & Construction
Bridge Reinforcement
Strengthening existing structures with FRP wraps
Seismic Retrofitting
Column wrapping for earthquake resistance
Rebar Replacement
Corrosion-free reinforcement for concrete
Architectural Panels
Lightweight, durable building facades
Utility Poles
Non-conductive, weather-resistant alternatives
Wind Turbine Blades
Large-scale renewable energy structures

## Slide 21
Testing & Quality Control
Non-Destructive Testing (NDT)
Ultrasonic inspection - detect voids and delaminations
Thermography - identify subsurface defects
Radiography - internal structure examination
Mechanical Testing
Tensile, compression, and shear tests
Fatigue and impact resistance evaluation
Interlaminar shear strength testing
Environmental Testing
Moisture absorption and aging studies
Temperature cycling and UV exposure

## Slide 22
Selection Criteria for Composites
1
Define performance requirements (strength, stiffness, weight)
2
Identify environmental conditions (temperature, moisture, chemicals)
3
Evaluate manufacturing feasibility and complexity
4
Consider cost constraints (material, processing, tooling)
5
Assess design flexibility and shape requirements
6
Analyze lifecycle costs including maintenance
7
Review certification and regulatory compliance
8
Perform comparative analysis with alternatives

## Slide 23
Future Trends & Innovations
Nano-composites
Enhanced properties through nano-scale reinforcement
Bio-based Composites
Sustainable natural fiber and bio-resin matrices
Self-healing Materials
Autonomous damage repair capabilities
Multifunctional Composites
Integrated sensors, energy storage, thermal management
Automated Manufacturing
AI-driven layup, 3D printing of composites
Recyclable Thermoplastics
Improved sustainability and circular economy

## Slide 24
Case Study: Boeing 787 Dreamliner
First commercial aircraft with >50% composite structure by weight
Composite Usage
Carbon fiber reinforced polymer for fuselage and wings
Weight Savings
20% lighter than equivalent aluminum structure
Benefits
Improved fuel efficiency, larger windows, better cabin pressure
Manufacturing
One-piece fuselage barrel sections reduce assembly
Challenges
Higher upfront cost, specialized repair requirements
Impact
Set new standard for commercial aviation composites

## Slide 25
KEY TAKEAWAYS
Composites offer unmatched performance advantages
Material selection depends on specific application requirements
Consider manufacturing, cost, and lifecycle factors
Future innovations will expand composite applications
Proper design and quality control are essential for success