## Slide 1
FRICTIONLESS MAGNETIC GEAR SYSTEMS
Next-Generation Power Transmission Technology

## Slide 2
OVERVIEW
Introduction & Fundamentals
Operating Principles
Types of Magnetic Gears
Key Benefits
Limitations & Challenges
Applications & Future Outlook

## Slide 3
WHAT ARE MAGNETIC GEARS?
Magnetic gears transmit torque between rotating shafts using magnetic fields instead of mechanical teeth contact
Unlike conventional gears that rely on physical mesh, magnetic gears use the attractive and repulsive forces between permanent magnets to transfer power

## Slide 4
HISTORICAL DEVELOPMENT
1901
First magnetic gear concept patented
1940s-60s
Limited development due to weak permanent magnets
1980s
Breakthrough with neodymium magnets (NdFeB)
2001
Coaxial magnetic gear design by Atallah
2010s-Present
Rapid advancement in applications

## Slide 5
OPERATING PRINCIPLE
Magnetic Field Interaction
Permanent magnets on rotors create strong magnetic fields
Opposite poles attract, like poles repel
Magnetic coupling creates torque transmission
Air gap separates components - NO physical contact

## Slide 6
GEAR RATIO IN MAGNETIC GEARS
Gear Ratio = Number of Pole Pairs on Output / Number of Pole Pairs on Input
Determined by magnet pole pair count
Typical ratios: 3:1 to 15:1 (can go higher)
Fixed ratio based on physical design

## Slide 7
TYPE 1: RADIAL FLUX MAGNETIC GEARS
CHARACTERISTICS
Magnetic flux flows radially
Simple design
Compact structure
Most common type
APPLICATIONS
Electric vehicles
Wind turbines
Industrial machinery

## Slide 8
TYPE 2: AXIAL FLUX MAGNETIC GEARS
CHARACTERISTICS
Flux flows axially
Pancake-like form
Higher torque density
Better cooling
ADVANTAGES
Compact axial length
High power density
Modular design

## Slide 9
TYPE 3: COAXIAL MAGNETIC GEARS
The Most Advanced Design
Three concentric rotors with pole pieces between them
Highest torque density of all magnetic gear types
Input and output shafts are coaxial (aligned)
Magnetic field modulation creates effective gear ratio
Can achieve ratios of 5:1 to 20:1 efficiently

## Slide 10
KEY BENEFITS

## Slide 11
1. ZERO MECHANICAL FRICTION
IMPACT
No wear and tear on components
RESULT
Extended service life (10-20 years+)
Elimination of friction-related losses
No need for lubricants or cooling fluids
Reduced maintenance requirements
Lower operating costs over lifetime

## Slide 12
2. SUPERIOR EFFICIENCY
Chart: 
| Mechanical Gears | Magnetic Gears
Efficiency | 93 | 99

## Slide 13
3. INHERENT OVERLOAD PROTECTION
When torque exceeds limit, magnets slip without damage
Acts like a magnetic clutch during overload
Protects downstream equipment from damage
No catastrophic failure like gear tooth breakage
System automatically re-engages when overload clears

## Slide 14
4. SILENT OPERATION
No gear meshing noise or vibration
Ideal for noise-sensitive environments
Improved workplace comfort
Reduced acoustic emissions
Noise reduction: 20-30 dB compared to mechanical gears

## Slide 15
5. MISALIGNMENT TOLERANCE
Can tolerate small misalignments without performance loss
Air gap provides flexibility in installation
Reduced precision requirements for mounting
Lower installation and assembly costs

## Slide 16
6. HERMETICALLY SEALED OPERATION
CAPABILITY
Torque transmitted through non-magnetic barrier
Complete isolation of environments
No seals or gaskets needed
APPLICATIONS
Chemical processing
Food & pharma
Hazardous environments

## Slide 17
LIMITATIONS & CHALLENGES

## Slide 18
1. HIGH INITIAL COST
Cost: 3-5x higher than equivalent mechanical gears
Expensive rare-earth permanent magnets (NdFeB)
Complex manufacturing processes
Specialized assembly procedures
ROI depends on reduced maintenance and energy savings

## Slide 19
2. LARGER SIZE & WEIGHT
Lower torque density than modern mechanical gears
Require larger diameter to achieve same torque
Heavy permanent magnets increase weight
Typically 30-50% larger and heavier than mechanical equivalents
Space constraints in compact applications

## Slide 20
3. TEMPERATURE SENSITIVITY
NdFeB magnets lose strength above 150-200°C
Permanent demagnetization at Curie temperature
Performance degradation in high-temperature applications
Requires active cooling in some cases
Alternative high-temp magnets (SmCo) are more expensive

## Slide 21
4. LIMITED MAXIMUM TORQUE
Pull-out torque limit before magnetic slip occurs
Not suitable for very high-torque applications
Current practical limit: ~10,000 Nm
Mechanical gears can handle much higher torques
Best suited for medium-torque applications

## Slide 22
5. AIR GAP SENSITIVITY
Torque density decreases exponentially with air gap
Requires precise manufacturing tolerances
Typical air gap: 1-3 mm
Any increase reduces performance significantly
Vibration and thermal expansion can affect gap

## Slide 23
6. DEMAGNETIZATION RISK
Permanent magnets can lose magnetization over time
Causes: excessive heat, strong external fields, mechanical shock
Irreversible performance degradation
Difficult and expensive to repair or remagnetize
Requires protective design measures

## Slide 24
APPLICATION: WIND TURBINES
Replace heavy, maintenance-intensive gearboxes
Reduce downtime and maintenance costs
Improve reliability in harsh offshore environments
Overload protection during wind gusts
Challenge: Scaling to multi-MW turbines requires very large diameters

## Slide 25
APPLICATIONS: EVs & ROBOTICS
ELECTRIC VEHICLES
Silent powertrain
High efficiency
Compact in-wheel motors
Reduced drivetrain complexity
ROBOTICS
Precise control
Backdriveable joints
Safe human interaction
No backlash

## Slide 26
COMPARATIVE SUMMARY
PARAMETER | MECHANICAL GEARS | MAGNETIC GEARS
Efficiency | 93-96% | 97-99%
Maintenance | Regular | Minimal
Noise Level | High | Very Low
Overload Protection | None | Inherent
Cost | Low | High
Weight | Moderate | Heavy
Torque Capacity | Very High | Limited

## Slide 27
FUTURE OUTLOOK
Cost reduction through manufacturing advances
Development of alternative magnet materials
Improved torque density through design optimization
Growing adoption in renewable energy and EVs
Integration with direct-drive systems
Hybrid designs combining magnetic and mechanical elements

## Slide 28
CONCLUSION
Magnetic gears offer revolutionary advantages in efficiency, reliability, and maintenance, but face challenges in cost and torque capacity. Best suited for applications where their unique benefits justify the premium.