## Slide 1
SILICA CHIP DESIGNING
From Silicon Wafers to Advanced Integrated Circuits

## Slide 2
Contents
1
Introduction to Silica Chips
2
Silicon Properties & Why Silicon
3
Chip Design Process Overview
4
Front-End Design (Logic Design)
5
Back-End Design (Physical Design)
6
Fabrication Processes
7
Testing & Validation
8
Advanced Technologies & Future Trends

## Slide 3
What is a Silica Chip?
Definition
A silica chip, or silicon chip, is an integrated circuit manufactured from a thin slice of crystalline silicon. It contains billions of microscopic transistors that process and store digital information.
Key Components
Transistors, interconnects, dielectric layers, metal layers, and substrate form the foundation of modern computing.

## Slide 4
Why Silicon?
Abundance
Second most abundant element in Earth's crust, making it cost-effective
Semiconductor Properties
Perfect electrical characteristics for switching and amplification
Silicon Dioxide
Forms excellent insulating layer (SiO₂) for device isolation
High Melting Point
Withstands high processing temperatures (1414°C)

## Slide 5
Chip Design Process Overview
1
Specification
2
Architecture
3
RTL Design
4
Verification
5
Synthesis
6
Physical Design
7
Fabrication
8
Testing

## Slide 6
Front-End Design: Specification
Define functional requirements and performance targets
Power consumption constraints and thermal limits
Area and cost targets
Interface protocols and standards compliance
Operating frequency and voltage requirements
Critical Success Factor: Clear specifications prevent costly redesigns later in the process.

## Slide 7
Architecture Design
System Partitioning
Divide design into functional blocks and modules
Data Path Design
Define how data flows through the system
Control Logic
Specify state machines and control signals
Memory Hierarchy
Cache, RAM, registers organization

## Slide 8
RTL Design (Register Transfer Level)
Hardware Description Languages
Verilog: C-like syntax, widely adopted in industry
VHDL: Strongly typed, used in aerospace and defense
SystemVerilog: Enhanced verification capabilities
Key Concepts
Registers, combinational logic, sequential logic, finite state machines, pipelining, and clock domains.
Example: Verilog Module
module adder(
input [7:0] a, b,
input cin,
output [7:0] sum,
output cout
);
assign {cout,sum} =
a + b + cin;
endmodule

## Slide 9
Functional Verification
Verification Techniques
Simulation: Digital waveform analysis using testbenches
Formal Verification: Mathematical proof of correctness
Emulation: Hardware acceleration for faster verification
Coverage Analysis: Ensure all code paths are tested
Assertion-Based Verification: Runtime property checking

## Slide 10
Logic Synthesis
RTL Code
Synthesis Tool
Gate-Level Netlist
Synthesis Optimizations:
Area optimization: Minimize gate count and chip area
Timing optimization: Meet clock frequency targets
Power optimization: Reduce dynamic and static power

## Slide 11
Back-End Design
Physical Implementation

## Slide 12
Floorplanning
Objectives
Partition chip area into functional blocks
Position macros (RAM, ROM, IP blocks)
Define power grid and I/O pad locations
Create routing channels between blocks
Minimize wire length and congestion

## Slide 13
Cell Placement
1
Global Placement
Rough positioning to minimize total wire length
2
Legalization
Align cells to grid and remove overlaps
3
Detailed Placement
Fine-tune positions for timing and routability

## Slide 14
Clock Tree Synthesis (CTS)
Purpose: Distribute clock signal to all sequential elements with minimal skew
Key Metrics
Clock Skew: Timing difference between clock arrivals
Insertion Delay: Source to sink latency
Transition Time: Signal rise/fall time
CTS Techniques
H-Tree topology
X-Tree topology
Buffer insertion
Clock gating for power

## Slide 15
Routing
Global Routing
Assigns nets to routing regions and determines approximate paths. Creates routing guides for detailed routing.
Detailed Routing
Assigns specific metal layers and tracks. Ensures DRC compliance and minimizes crosstalk and resistance.
Routing Challenges:
Minimize wire RC delay and signal integrity issues
Avoid routing congestion in high-density areas
Meet design rule constraints for manufacturability

## Slide 16
Physical Verification
DRC (Design Rule Check)
Minimum width and spacing
Via overlap requirements
Metal density rules
LVS (Layout vs Schematic)
Netlist matching
Device parameter verification
Connectivity checking
ERC (Electrical Rule Check)
Antenna effect violations
Electromigration limits
Power/ground connectivity

## Slide 17
Static Timing Analysis (STA)
STA verifies that all paths in the design meet timing requirements without running simulations.
Key Timing Checks:
Setup Time: Data must be stable before clock edge
Hold Time: Data must remain stable after clock edge
Clock-to-Q Delay: Register output delay
Propagation Delay: Combinational logic delay
Timing Paths:
Register-to-Register (most common)
Input-to-Register
Register-to-Output
Input-to-Output (combinational)

## Slide 18
Fabrication Process
From Design to Silicon

## Slide 19
Silicon Wafer Processing
1
Wafer Preparation
Crystal growth (Czochralski process), slicing, polishing
2
Oxidation
Grow silicon dioxide layer (thermal oxide)
3
Photolithography
Pattern transfer using UV light and photoresist
4
Etching
Remove unwanted material (wet or dry etch)
5
Doping
Ion implantation or diffusion to create N/P regions
6
Metallization
Deposit and pattern metal interconnect layers

## Slide 20
Photolithography Process
Critical for defining nanometer-scale features
Clean wafer surface
Spin-coat photoresist (light-sensitive polymer)
Soft bake to remove solvents
Align mask with wafer
Expose to UV light through mask
Develop photoresist (remove exposed or unexposed regions)
Hard bake to harden remaining photoresist
Etch or implant through pattern
Strip remaining photoresist

## Slide 21
Etching Techniques
Wet Etching
Uses liquid chemical solutions. Isotropic (etches in all directions). Lower cost, less precise.
Common Etchants:
HF (hydrofluoric acid) for SiO₂
KOH for silicon
H₃PO₄ for silicon nitride
Dry Etching (Plasma)
Uses plasma or reactive gases. Anisotropic (directional). High precision for nanoscale features.
Types:
RIE (Reactive Ion Etching)
Deep RIE for high aspect ratios
ICP (Inductively Coupled Plasma)

## Slide 22
Doping Methods
Purpose: Create N-type and P-type semiconductor regions
Ion Implantation
Advantages: Precise control, room temperature, selective doping
Challenges: Lattice damage requires annealing
Diffusion
Advantages: Uniform doping, less damage
Challenges: Less precise, requires high temperature

## Slide 23
Metal Layers & Interconnects
Modern chips use 10-15 metal layers for routing signals and power delivery.
Materials Used
Copper (Cu): Lower resistance, better performance
Aluminum (Al): Traditional, easier processing
Tungsten (W): Vias and contacts
Barrier layers: Prevent metal diffusion
Fabrication Steps
Deposit dielectric (SiO₂, low-k materials)
Pattern via holes
Deposit barrier and seed layers
Electroplate copper
CMP (Chemical-Mechanical Polish)

## Slide 24
Process Nodes & Technology Scaling
Node
Year
Transistor Count
180nm
1999
Millions
90nm
2004
Tens of millions
45nm
2007
Hundreds of millions
22nm
2012
Billions
7nm
2018
Tens of billions
3nm
2022
50+ billion
Moore's Law: Transistor count doubles approximately every 2 years

## Slide 25
Testing & Quality Assurance
Ensuring Chip Functionality

## Slide 26
Wafer-Level Testing
Parametric Testing
Verify transistor characteristics, leakage currents, threshold voltages
Functional Testing
Test logic functionality using probe cards
Burn-In Testing
Stress testing at elevated temperatures and voltages
Binning
Sort dies by performance grade and yield

## Slide 27
Package-Level Testing
Post-Packaging Tests
Final functional verification
Speed binning (frequency sorting)
Power consumption measurement
Temperature cycling tests
ESD (Electrostatic Discharge) testing
Quality Metrics
Yield: Percentage of functional chips
DPPM: Defects Per Million
MTBF: Mean Time Between Failures
Reliability testing (1000-10000 hours)

## Slide 28
Design for Testability (DFT)
Scan Chains
Convert flip-flops into shift registers for controllability and observability
BIST (Built-In Self-Test)
On-chip test pattern generation and response analysis
Boundary Scan (JTAG)
IEEE 1149.1 standard for testing interconnects and peripherals
Memory BIST
Dedicated logic for testing embedded memories

## Slide 29
Power Management in Chip Design
Dynamic Power
P = α × C × V² × f
Switching activity (α)
Capacitance (C)
Voltage (V)
Frequency (f)
Static Power (Leakage)
Subthreshold leakage
Gate oxide leakage
Junction leakage
Increases with temperature

## Slide 30
Power Reduction Techniques
Clock Gating
Disable clock to idle blocks
Power Gating
Shut off power to unused modules
DVFS
Dynamic Voltage and Frequency Scaling
Multi-Vt Cells
Use high-Vt cells in non-critical paths
Operand Isolation
Prevent unnecessary switching
Low-Power Synthesis
Optimize for power during design

## Slide 31
Advanced Technologies
Pushing the Boundaries

## Slide 32
FinFET Technology
What is FinFET?
Fin Field-Effect Transistor - a 3D transistor architecture where the channel is formed as a thin vertical fin, allowing the gate to wrap around three sides for better control.
Advantages
Reduced short-channel effects
Lower leakage current
Better performance at lower voltages
Timeline
2011: Intel introduces FinFET (22nm)
2012: TSMC and Samsung adopt
Standard for 14nm and below
Evolved into GAA (Gate-All-Around) at 3nm

## Slide 33
EUV Lithography
Extreme Ultraviolet (EUV) Lithography
Wavelength: 13.5 nm (vs 193 nm for traditional DUV)
Higher Resolution
Enables <7nm feature sizes with fewer masking steps
Reflective Optics
Uses mirrors instead of lenses due to wavelength absorption
Plasma Source
Tin droplets bombarded by laser to generate EUV light
Vacuum Environment
Required due to EUV absorption by air and materials

## Slide 34
Future Trends in Chip Design
3D IC Stacking
Vertical integration of multiple dies using TSVs (Through-Silicon Vias)
Chiplets
Modular approach with specialized dies connected via advanced packaging
Photonic Integration
Optical interconnects for higher bandwidth and lower power
AI-Driven Design
Machine learning for optimization and automated design closure
Quantum Computing
Superconducting qubits and topological quantum computing
Carbon Nanotubes
Potential replacement for silicon in future transistors

## Slide 35
Silica Chip Design
A Journey from Sand to Supercomputing