## Slide 1: Firmware is the new Black – Analyzing Past 3 years of BIOS/UEFI Security Vulnerabilities
Bruce Monroe & Rodrigo Rubira Branco (@bsdaemon) & Vincent Zimmer (@vincentzimmer)
{ bruce.monroe || rodrigo.branco || vincent.zimmer } @ intel.com

## Slide 2
In recent years we witnessed the rise of firmware-related vulnerabilities, likely a direct result of increasing adoption of exploit mitigations in major/widespread operating systems, including for mobile phones. Pairing that with the recent (and not so recent) leaks of government offensive capabilities abusing supply chains and using physical possession to persist on compromised systems, it is clear that firmware is the new black in security. This research looks into BIOS/UEFI platform firmware, trying to help making sense of the threat. We present a threat model, discuss new mitigations that could have prevented the issues and offer a categorization of bug classes that hopefully will help focusing investments in protecting systems (and finding new vulnerabilities). Our data set comprises of 90+ security vulnerabilities handled by Intel Product Security Incident Response Team (PSIRT) in the past 3 years and the analysis was manually performed, using white-box and counting with feedback from various BIOS developers within the company (and security researchers externally that reported some of the issues - most of the issues were found by internal teams, but PSIRT is involved since they were found to also affect released products).
ABSTRACT
Notes: This is our abstract Bruce

## Slide 3
DISCLAIMER
Intel has official documentation that is highly comprehensive and should be used to make technical decisions related
to Intel’s technologies. To have a high-level of accuracy for such documentation, lots of reviews are performed
The accuracy of this talk can’t be compared and should not be used to compare with official documentation. We
are going to discuss directions, strategies and initiatives being proposed, giving recommendations to OEMs, researchers
and customers but everything should be treated as *OUR* opinion instead of official statements
There possibly are other initiatives and focus areas that we are not at liberty to talk about or that we are even unaware
of, so this should not be considered the full scope of the problem, but instead, *OUR* vision of it
This talk is about BIOS/UEFI security. We are not pedantic on terminology (since we accept that the majority outside
of Intel have a harder time to know/differentiate what is the responsibility of different components of the platform in
order to guarantee the security of it). As so, we did include things that are *NOT* directly related to errors in BIOS/UEFI
per-se, but that somehow affected the expectations for it
Notes: The last line of the disclaimer was added because in the classes I’ve added cache overwriting SMM area, fuses not properly setup and priority decoding for overlapping ranges (the LAPIC bug), which are outside of the expectation for BIOS/UEFI itself, but did affect BIOS/UEFI security.
Bruce

## Slide 4
Agenda
BIOS/UEFI background
BIOS/UEFI ecosystem
BIOS/UEFI security technologies
Dataset & Methodology
Bug classes (a proposal for UEFI)
Vulnerability distribution (by bug classes)
Platform Firmware Threat Modelling
Future
Notes: Bruce

## Slide 5
UEFI Background
UEFI – Unified Extensible Firmware Interface old school terms…(BIOS)
First up root of trust on the system
It hands over control to the operating system
  Rest of the magic then occurs ;)
UEFI Membership spans the compute spectrum
http://uefi.org/members
UEFI – sets up the platform to run…
Notes: Bruce

## Slide 6: Where is UEFI firmware
SMM / BIOS
CPU
App
OS
App
VM
App
OS
App
VM
VMM / Hypervisor
Memory
Peripherals
Firmware
Hardware
Platform
Privilege
BIOS & OS/VMM share access, but not trust
UEFI + PI SMM
Hypervisor can grant VM direct hardware access
DMA
A specific Peripheral may have its own processor, and its own firmware, which is undetectable by host CPU/OS.
Notes: Bruce

## Slide 7: What’s in UEFI
Notes: Bruce

## Slide 8
UEFI Ecosystem is an “Onion”. Layers upon layers…
Peel the onion and you have:
  Tianocore (Open Source EDK II) Intel is the sole maintainer
  IBV – Independent BIOS Vendors
  OEM – Other Equipment Manufacturers (The folks building your systems)
  ODM – Original Design Manufacturer
  Consumers (deliberate action to download/install updates)
If a vuln mitigation goes out it has to navigate the onion
  Additional update lag time is introduced because end users have to take deliberate action to download/install updates
UEFI Ecosystem Overview
Notes: Bruce

## Slide 9
UEFI Ecosystem
Notes: Bruce

## Slide 10
UEFI.org is a standards body
UEFI is a specification
About 2 years ago UEFI.org stood up USRT
  USRT – is Unified Security Response Team
Sea change. UEFI had never taken a stance on implementations.
They Are Now…
History
Notes: Bruce

## Slide 11
USRT is comprised by Firmware Engineers from member companies
To report a security issue in UEFI Firmware implementation from a vendor:
  Send email to security@uefi.org
  Encrypt sensitive info with their PGP public key - security@uefi.org
Please provide as much information as possible, including:
  The products and versions affected
  Detailed description of the vulnerability
  Steps to demonstrate the vulnerability or reproduce the exploit, including specific configurations or peripherals, if relevant
  Potential impact of the vulnerability, when exploited
  Information on known exploits
UEFI USRT
Notes: Bruce

## Slide 12
Tianocore EDK II that is solely maintained by Intel is in bug bounty scope
Send vulnerability report to secure@intel.com
  Encrypt using PGP Public Key of secure@intel.com
Intel Bug Bounty Program is Private Invite Only
If you find a good quality bug in Tianocore we will extend an invite providing you agree to abide by Intel Bug Bounty program terms
  Note: you need to be invited to be eligible
You can find more information on the Intel Bug bounty program online
Full participation guidelines https://security-center.intel.com/docs/BugBountyParticipationGuidelines.pdf
Reporting to Intel Bug Bounty
Notes: Bruce

## Slide 13
The Intel Bug Bounty Program is a Private Invite Only program
If the security vulnerability is in open source implementation of Tianocore solely maintained by Intel
  It’s Eligible for the Intel Bug Bounty Program administered by HackerOne
You must be invited to join via HackerOne platform
Vulnerability Severity | Intel Software | Intel Firmware | Intel Hardware
Critical | Up to $7,500 | Up to $10,000 | Up to $30,000
High | Up to $2,500 | Up to $5,000 | Up to $10,000
Medium | Up to $1,000 | Up to $1,500 | Up to $2,000
Low | Up to $500 | Up to $500 | Up to $1,000
Intel Bug Bounty Recap
Notes: Bruce

## Slide 14
The EFI Developer Kit II (EDKII) provides an open source implementation http://www.tianocore.org/
  Core features https://github.com/tianocore/edk2
  Platform examples https://github.com/tianocore/edk2-platforms
Reporting security issues on open source https://github.com/tianocore/tianocore.github.io/wiki/Reporting-Security-Issues
  Advisories https://www.gitbook.com/book/edk2-docs/security-advisory/details
EDKII Bugzilla
Notes: Bruce -> Vincent transition

## Slide 15
UEFI is the specification
EDK II is the code
Protect
Detect
Recover
System
Firmware
Use of EDKII Defenses
Notes: Vincent

## Slide 16
CPU/SOC
(Intel)
Start Block PEI
(OEM)
Policy
Policy Engine
Enforces
BIOS DXE/UEFI
(OEM)
OS Loader/Kernel
(OSV)
Policy
Policy Engine
Enforces
Policy
Policy Engine
Enforces
OEM PI Verification
Using PI Signed
Firmware Volumes Vol 3, section 3.2.1.1
of PI 1.3 Specification
OEM UEFI 2.7 Secure Boot
Chapter 27.2 of
The UEFI 2.4 Specification
Intel® Device Protection Technology with Boot Guard
http://www.intel.com/content/dam/www/public/us/en/documents/product-briefs/4th-gen-core-family-mobile-brief.pdf
Executable
Executable
Executable
Intel® Boot Guard
Measure
Measure
Measure
Protect
Detect
Fully Verified Boot Sequence
Notes: Vincent

## Slide 17
UEFI authenticate OS loader (pub key and policy)
Check signature of before loading
UEFI Secure boot will stop platform boot if signature not valid (OEM to provide remediation capability)
UEFI will require remediation mechanisms if boot fails
UEFI PI will measure OS loader & UEFI drivers into TPM (1.2 or 2.0) PCR (Platform Configuration Register)
TCG Trusted boot will never fail
Incumbent upon other software to make security decision using attestation
UEFI Firmware
UEFI OS Ldr, Drivers
Kernel
Drivers
Apps
TPM
record in PCR
UEFI
Trusted Versus Secure Boot
Protect
Detect
Notes: Vincent

## Slide 18
UEFI Secure and TCG Measured boot - Upper layer API’s defined in UEFI and TCG spec
  Implementation source + document for UEFI Secure & TPM measured boot
    https://github.com/tianocore/edk2/tree/master/SecurityPkg
    https://firmware.intel.com/sites/default/files/resources/A_Tour_Beyond_BIOS_Implementing_TPM2_Support_in_EDKII.pdf
  http://bluestop.org/edk2/docs/specs/A_Tour_Beyond_BIOS_into_UEFI_Secure_Boot_White_Paper.pdf
Signed updates - Capsules defined in UEFI Spec
  Signed updates required by NIST 800-147 http://csrc.nist.gov/publications/nistpubs/800-147/NIST-SP800-147-April2011.pdf for core and NIST-193 http://csrc.nist.gov/publications/drafts/800-193/sp800-193-draft.pdf for platform components
  https://github.com/tianocore/edk2/tree/master/SignedCapsulePkg
  https://github.com/tianocore-docs/Docs/raw/master/White_Papers/A_Tour_Beyond_BIOS_Capsule_Update_and_Recovery_in_EDK_II.pdf
EDKII Defenses (1/3)
Protect
Recover
Detect
Notes: Vincent

## Slide 19
Defense in depth mechanisms of UEFI Core
  NX, ASLR, stack canaries during pre-OS https://www.gitbook.com/book/edk2-docs/a-tour-beyond-bios-memory-protection-in-uefi-bios/details
Hardened SMM
  Implementing the Windows SMM Mitigation Table (WSMT) https://github.com/tianocore-docs/Docs/raw/master/White_Papers/A_Tour_Beyond_BIOS_Secure_SMM_Communication.pdf
  A_Tour_Beyond_BIOS_Securiy_Enhancement_to_Mitigate_Buffer_Overflow_in_UEFI https://github.com/tianocore-docs/Docs/raw/master/White_Papers/A_Tour_Beyond_BIOS_Securiy_Enhancement_to_Mitigate_Buffer_Overflow_in_UEFI.pdf
And lock-box protocol, user identification, password, and random number generation
Overall dev BKM (Best Known Methods)
  Security BKM https://github.com/tianocore-docs/Docs/raw/master/White_Papers/A_Tour_Beyond_BIOS_Security_Design_Guide_in_EDK_II.pdf
EDKII Defenses (2/3)
Protect
Recover
Notes: Vincent

## Slide 20
Intel STM (SMI Transfer Monitor): https://firmware.intel.com/content/smi-transfer-monitor-stm
BIOS Guard (PFAT): SMM compromises do not directly lead to flash access (persistence)
Other SMM protections:
Continued SMM Defenses
Protect
Notes: Vincent

## Slide 21
VT-d boot protection
  https://lists.01.org/pipermail/edk2-devel/2017-April/009454.html https://firmware.intel.com/sites/default/files/resources/A_Tour_Beyond_BIOS_Using_Intel_VT-d_for_DMA_Protection.pdf
And to pull things together - Full open source EDKII-based platforms
  Quark https://github.com/tianocore/edk2/tree/master/QuarkPlatformPkg
  Atom BYT https://github.com/tianocore/edk2-platforms/tree/minnowboard-max-udk2015
  Atom APL https://github.com/tianocore/edk2-platforms/tree/devel-MinnowBoard3-UDK2017
  Intel KBL https://github.com/tianocore/edk2-platforms/tree/devel-MinPlatform core platform tree
Atom and core platforms based upon Intel Firmware Support Package (FSP)
  https://github.com/IntelFsp/FSP
  https://firmware.intel.com/sites/default/files/A_Tour_Beyond_BIOS_Using_the_Intel_Firmware_Support_Package_with_the_EFI_Developer_Kit_II_%28FSP2.0%29.pdf
  http://www.apress.com/us/book/9781484200711
Very through training package made available by Intel’s ATR* – covers chipsec
  https://github.com/advanced-threat-research/firmware-security-training
  Intel’s ATR moved from SeCoE to Intel Security and is now part of McAfee
EDKII Defenses (3/3)
Protect
Detect
Recover
Notes: Vincent

## Slide 22
It is quite hard to provide really good analysis of datasets related to security issues:
  A must see if somehow you wonder why: https://media.blackhat.com/us-13/US-13-Martin-Buying-Into-The-Bias-Why-Vulnerability-Statistics-Suck-Slides.pdf
We used Intel’s PSIRT Data in different ways:
  For the past 3 years (124 issues related to BIOS/Firmware), to give an ‘idea’ of the amount of issues (which adds attrition bias as well)
  For as long as we could find (Circa 2007), to generate taxonomy
Intel’s PSIRT data include issues found internally (vendor selection bias) that somehow were identified to affect released products
  It does not mean every internally found issue is there
  The way the data is capture changed along the years (hopefully for better), but that is one of the mistakes clearly stated in the aforementioned presentation 
  We constantly receive reports for issues that affect a specific OEM-only (and as so, have nothing to do with Intel – please, keep involving us, it is helpful!): We counted those too, but obviously, lots of issues are not reported to us as well (that also adds a researcher selection bias, since some researchers always involve us and as so, whatever issues they are finding, are accounted for, but not all researchers do that)
  PSIRT does sometimes group multiple issues under one case (specially internal ones), and as so, the count itself also added an abstraction bias
  For some other cases, issues are divided in multiple cases (given it potentially spawning multiple different actions): We tried to clean the obvious cases
  We only considered the confirmed issues that affect at least one product, therefore there is also publication bias
Total number of issues considered/used: 77 issues
Dataset & Methodology (1/2)
Notes: Vincent -> Rodrigo transition

## Slide 23
With so many problems in the dataset, does it have any value?
  Yes, but not to compare platforms (so we do not include such information)
  Yes, for defining a taxonomy (so we did generate/propose one)
  Yes, to help defining next steps/future strategies (so we did do that)
  Maybe, to define trends (as in: are those kind of problems getting more external attraction?)
  No, if you want to say that there are more bugs (not bugs being reported, which is the previous point) now than few years back -> DO NOT USE THE DATA FOR THAT PURPOSE 
Dataset & Methodology (2/2)
Notes: Rodrigo

## Slide 24
Those bugs are not BIOS-bugs per-se, but they do affect platform security and what is expected from BIOS (we did not consider them in the total count presented, and we did group those in the taxonomy as a single class: ‘HW bugs’). Some examples:
  LAPIC bug (memory range overlapping and decoding priorities leading to SMRAM access)
  SMM memory written-back cached data from Ring0 leading to SMRAM access
  Fuse mis-configuration for BootGuard leading to platform compromise (See for example “Safeguarding rootkits: Intel BootGuard” presented at ZeroNights 2016 (https://dsec.ru/upload/medialibrary/82b/82b222a0ab6470a724108b42208f0630.pdf)
HW Bugs?
Notes: Rodrigo

## Slide 25
We do not claim it to be a comprehensive list, but it is comprehensive enough to cover all PSIRTs received by Intel
  Many bugs might fit multiple classes (since one problem might lead to another, we use the first in the chain to aggregate)
  Help evolve this list
Notice that we grouped together things that are a bit more classical software cases (for example, not properly validating untrusted input)
  But we still called out ones that have some specificities due to the expectations for the whole platform security
The main intention: be able to easily define a class for a given issue and to remove the sentiment (shared by many researchers) that BIOS security is something obscure
  Notice that when we group the classes per the number of reported issues in each 
Proposal of Bug Classes (1/2)
The main complexity is the sheer number of platform-specific configurations
Notes: Rodrigo

## Slide 26
Inconsistent power-transition checks
  Bad Initialization State (secrets kept in memory, assumption of certain system state)
  S3 Boot Script
Race Condition
  Enabling protection mechanisms (including disabling/enabling certain HW elements, including wrong module launching order)
  Time of Check/Time of Use (TOCTOU) Race Conditions
Trusting input (from less privileged entities in the platform, or having different assets configured by different threat vectors)
  Could lead to race conditions (double fetches and TOCTOUs, for example if a pointer is pointing to unprotected memory area and therefore can be arbitrarily modified after any checks)
Measurement failures
  Not measuring certain modules
  Accepting signed updates, but for the wrong platform due to using same keys
  Accepting to load certain modules in the wrong time (when certain assets are not properly protected)
  Failing to identify a measurement error/problem
Platform capability not properly configured
  Locks not set, devices not properly initialized, features not disabled, etc
Security of meaningful assets exposed to untrusted entities
  E.g.: UEFI variables
HW Misbehavior
  Wrongly defined architecture, micro-architecture, bad design, etc
  Platform components behaving differently than specified
Proposal of Bug Classes (2/2)
Notes: Rodrigo

## Slide 27
Inconsistent power-transition checks
  Bad Initialization State (secrets kept in memory, assumption of certain system state)
  S3 Boot Script
Many talks mention the S3 Boot Script vulnerability and public exploits/write-ups are available (http://blog.cr4.sh/2015/02/exploiting-uefi-boot-script-table.html)
Some of the bugs in this category can be very subtle, like when a system is turned on a given code path is taken which copies certain data structures inside SMRAM for parsing, while when the system is coming back from resume the SMM code consumes external tables directly (therefore, wrongly trusting the runtime OS)
Examples (1/7)
Notes: Rodrigo

## Slide 28
Race Condition
  Enabling protection mechanisms (including disabling/enabling certain HW elements, including wrong module launching order)
  Time of Check / Time of Use TOCTOU Race Condition
A good example we saw was a third party option ROM being launched before EndOfDxe (lots of assets unprotected)
Another common case is SMM code validating input *before* copying it to protected memory (which could be altered after the checks)
  We experimenting with extending Simics to catch some of those (See: “Windows Kernel Race Condition Analysis While Accessing User-mode Data” paper in PoC || GTFO for some of our tests/experiments reproducing Project Zero’s work on Windows for similar problem) https://www.alchemistowl.org/pocorgtfo/pocorgtfo15.pdf
Examples (2/7)
Notes: Rodrigo

## Slide 29
Trusting input (from less privileged entities in the platform, or having different assets configured by different threat vectors)
  Could lead to race conditions (double fetches and TOCTOUs, for example if a pointer is pointing to unprotected memory area and therefore can be arbitrarily modified after any checks)
  Traditional code bugs apply here (like buffer and integer overflows)
Lots presented/found along the years by Intel’s ATR, SeCoE and other internal and external researchers
Many caught by our Excite Project (BIOS symbolic execution) (https://github.com/REhints/Publications/blob/master/Conferences/ZeroNights_2016/Excite_Project_ZN.pdf)
Examples (3/7)
Notes: Rodrigo

## Slide 30
Measurement failures
  Not measuring certain modules
  Accepting signed updates, but for the wrong platform due to using same keys
  Accepting to load certain modules in the wrong time (when certain assets are not properly protected)
  Failing to identify a measurement error/problem
Two real examples we’ve seem:
  Client & Server parts using the same keys, meaning that an image from one would load in the other, but obviously bricking the platform
  TE (Terse Executables) are loaded correctly, but not measured since deeper parts check for specific PE header presence (but the boot succeeds)
Examples (4/7)
Notes: Rodrigo

## Slide 31
Platform capability not properly configured
  Locks not set, devices not properly initialized, features not disabled, etc
  Lots of times guidance is just not being followed
  Chipsec use by OEMs and consumers would identify most of these
  See the Chipsec Platform Security Assessment Framework
https://github.com/chipsec/chipsec
  Watch the talk in H2HC: “Betraying the BIOS: Where the guardians of the BIOS are failing” for real life recent examples . Callout to Alex Matrosov
Examples (5/7)
Notes: Rodrigo

## Slide 32
Security of meaningful assets exposed to untrusted entities
  E.g.: UEFI variables
At least one case we’ve seem included UEFI variables that control PK/KEK not requiring physical presence to be modified
  That essentially undermines Secure Boot
Some times, sample code has validation features that should be disabled/removed from production versions, such as a UEFI variable that sets the policy responsible for configuring EISS (also known as SMM_BWP, which essentially opens the flash for writes from outside of SMM) bit in the SPI controller to be false
Examples (6/7)
Notes: Rodrigo

## Slide 33
HW Misbehavior
  Wrongly defined architecture, micro-architecture, bad design, etc
  Platform components behaving differently than specified
See Intel’s Erratas  We do our best, but things fail. Complexity and composition are security’s worst enemies
Examples of those:
  The Memory Sinkhole (by Christopher Domas in Black Hat USA 2015) https://www.blackhat.com/docs/us-15/materials/us-15-Domas-The-Memory-Sinkhole-Unleashing-An-x86-Design-Flaw-Allowing-Universal-Privilege-Escalation-wp.pdf
  Phrack article “Using SMM for Other Purposes” (http://phrack.org/issues/65/7.html) release of a weird cache behavior, followed by Joanna’s and Rafal’s work proving it was an exploitable vulnerability in “Attacking SMM Memory via Intel CPU Cache Poisoning” (http://invisiblethingslab.com/resources/misc09/smm_cache_fun.pdf)
  McAfee ATR work on “BARing the System” at Recon2017 (http://www.intelsecurity.com/advanced-threat-research/content/data/REConBrussels2017_BARing_the_system.pdf)
Examples (7/7)
Notes: Rodrigo

## Slide 34: Bug Class Distribution 2015-2017 (Past Week – Middle July)
Chart: Issues Distribution per Class: Total of 77 issues
| Inconsistent power-transition checks | Race Condition | Trusting input | Measurement failures | Platform capability not properly configured | Security of meaningful assets exposed to untrusted entities
 | 11 | 6 | 30 | 4 | 20 | 6
Notes: Rodrigo

## Slide 35: Bug Class Distribution per Year 2015-2017 (Past Week – Middle July)
Chart: Issues Distribution per Year
| Inconsistent power-transition checks | Race Condition | Trusting input | Measurement failures | Platform capability not properly configured | Security of meaningful assets exposed to untrusted entities
Total | 11 | 6 | 30 | 4 | 20 | 6
2015 | 5 | 4 | 5 | 0 | 3 | 0
2016 | 4 | 1 | 23 | 4 | 11 | 0
2017 | 2 | 1 | 2 | 0 | 6 | 6
Notes: Rodrigo

## Slide 36
“My house is secure” is almost meaningless
  Against a burglar? Against a meteor strike? A thermonuclear device?
“My system is secure” is almost meaningless
  Against what? To what extent?
Threat modeling is a process to define the goals and constraints of a (software) security solution
  Translate user requirements to security requirements
We used threat modeling for our UEFI / PI codebase
  We believe the process and findings are applicable to driver implementations as well as UEFI implementations in general
Rationale for a Threat Modeling
Notes: Rodrigo -> Vincent

## Slide 37
A Threat Model (TM) defines the security assertions and constraints for a product
  Assets: What we’re protecting
  Threats: What we’re protecting it against
  Mitigations: How we’re protecting our Assets
Use TM to narrow subsequent mitigation efforts
  Don’t only perform a secure review, fuzz test all interfaces
  Select the ones that are critical
TM is part science, part art, part experience, part nuance, part preference
  Few big assets vs lots of focused assets
Defining, using a Threat Modeling
Notes: Vincent

## Slide 38
PE/COFF
Operating System
Option ROM
SMM
This reg That reg Other bit
NIST
Security “Researchers”
UEFI, TCG, OSV
Internal Research
Source
BIOS Flash
Build tools
SMM
Boot flow
S3  S0
Internal Research
We don’t always get to choose our assets
Notes: Vincent

## Slide 39: Flash**
NIST SP800-147 says
  Lock code flash except for update before Exit Mfg Auth (Common Bugs: HW Misbehavior, Platform capability not properly configured)
  Signed update (>= RSA2048, SHA256) (Common Bugs: Security meaningful assets exposed to untrusted entities, Trusting input, Measurement Failures)
  High quality signing servers (Outside of the scope of the BIOS itself, but signing keys must be secret, etc)
  Without back doors (“non-bypassability”) (Common Bugs: A group of the above)
Threats
  PDoS – Permanent Denial of Service
    System into inefficient room heater
  Elevation of privileges
    Owning the system at boot is an advantage to an attacker
Known attacks
  CIH / Chernobyl 1999-2000
  Mebroni 2010
  Hacking Team 2015
  Various reputed government leaks (2016, 2017…)
Mitigations include
  Reexamining flash protection methods – use the best even if its new
  Using advanced techniques to locate and remove vulnerabilites
** or tomorrow’s equivalent NV storage
Notes: Vincent

## Slide 40: SMM
SMM is valuable because
  It’s invisible to System Software (including Anti Virus, etc)
  SMM sees all of system RAM (standard notion, without STM)
  Not too different from PCI adapter device firmware
  Most BIOS bugs are somehow related to getting SMM access (so all classes apply)
Threats
  Elevation of privileges
    View secrets or own the system by subverting RAM
Known attacks
  See e.g: Duflot, “Phrack Using SMM for Other Purposes and others”, Legbacore, McAfee’s Advanced Threat Research, Cr4sh
Mitigations include
  Validate “external” / “untrusted” input
  Remove calls from inside SMM to outside SMM
SMM
Notes: Vincent

## Slide 41: Resume from S3
ACPI says that we return the system to the S5S0 configuration at S3S0
  Must protect the data structures we record the cold boot config in (Common Bugs: Inconsistent power-transition checks, Race Condition, Security of meaningful assets exposed to untrusted entities)
Threats
  Changing data structures could cause security settings to be incorrectly configured leaving S3
  Reopen the other assets’ mitigated threats
Known attacks (McAfee ATR, Legbacore, cr4sh)
Mitigations include
  Store data in SMM -or-
  Store hash of data structures and refuse to resume if the hashes don’t compare
This reg That reg Other bit
Notes: Vincent

## Slide 42: Tool chain
Tools create the resulting firmware
  Rely on third party tools and home grown tools
  Incorrect or attacked tools leave vulnerabilities
  We did not add a class for those (instead we tried to tie the final bug to a class)
Threats
  Disabled signing, for example
Known attacks
  See e.g. Reflections on Trust, Ken Thompson**
Mitigation
  Difficult: For most tools, provided as source code
  Review for correct implementation
  Use static, dynamic code analysis tools
    PyLint for Python, for example
** CACM, Vol 27, No 8, Aug, 1984, pp. 761-763
Notes: Vincent

## Slide 43: Boot flow
Secure boot (Common Bugs: Measurement failures, Platform capability not properly configured, Security of meaningful assets exposed to untrusted entities, Race Condition)
  Authenticated variables
  Based on the fundamental crypto being correct
  Correct location for config data
Threats
  Run unauthorized op roms, boot loaders
  PDoS systems with bad config variables
Known attacks
Mitigations include
  Sanity check config vars before use, use defaults
  Reviews, fuzz checking, third party reviews, etc.
PE/ COFF
Notes: Vincent

## Slide 44
We can’t foresee the future, but there are lots of things that Intel is planning and that the overall industry can help!
  The release of a Platform Security Configuration Guide, independent of the BIOS Writer Guide (which currently already have a section for security)
  Release of more Chipsec and HSTI security checks
  Increase in mitigating technologies as part of the platform (some were discussed in this talk), to evolve the state-of-the-art
  Share of other initiatives, as we did for example with Excite (symbolic execution tool, currently used to automate finding SMM call-outs and having heavy investment)
What *you* can do to help? *OUR* CALL FOR ACTIONS!
  The ecosystem is complex, help naming the names and demonstrating the value to whoever cares about security
  Always question if attack demonstrated are against the state-of-the-art available, or are just one more configuration mistake (and mention the state-of-the-art if you are a researcher)
  Help us evolving such state-of-the-art: propose new attack classes (as some of you are already doing), propose architectural improvements: Dream high! Let us care about making it a reality 
  If you are an end-user: Those attacks are *NOT* complex. Understand and define your threat model, run the available tools and pressure your vendor!
Future
Notes: Vincent -> Rodrigo transition

## Slide 45
Lots of different individuals (and teams) inside and outside of Intel contribute to the evolution of UEFI security, some names from Intel (knowing very well we forgot many):
  Bulygin, Yuriy; Govindarajan, Sugumar; Mathews, John; Loucaides, John; Delgado, Brian; Yao, Jiewen; Frinzell, Aaron; Brannock, Kirk; Wolman, Ayellet; Rosenbaum, Lee; Bazhaniuk (see his presentation in H2HC this year)
Without them, this talk would not have been possible and we strongly appreciate their help, continuous feedback and work
To all the researchers that collaborate with Intel, directly or indirectly (yes, any form of report, including full-disclosure contributed to actions, decisions and direction changes) -> Thank you!
Acknowledgements
Notes: All

## Slide 46
QUESTIONS?
THE END! IS IT?
Bruce Monroe & Rodrigo Rubira Branco (@bsdaemon) & Vincent Zimmer (@vincentzimmer)
{ bruce.monroe || rodrigo.branco || vincent.zimmer } @ intel.com

## Slide 47
We can’t foresee the future, but there are lots of things that Intel is planning and that the overall industry can help!
  The release of a Platform Security Configuration Guide, independent of the BIOS Writer Guide (which currently already have a section for security)
  Release of more Chipsec and HSTI security checks
  Increase in mitigating technologies as part of the platform (some were discussed in this talk), to evolve the state-of-the-art
  Share of other initiatives, as we did for example with Excite (symbolic execution tool, currently used to automate finding SMM call-outs and having heavy investment)
What *you* can do to help? *OUR* CALL FOR ACTIONS!
  The ecosystem is complex, help naming the names and demonstrating the value to whoever cares about security
  Always question if attack demonstrated are against the state-of-the-art available, or are just one more configuration mistake (and mention the state-of-the-art if you are a researcher)
  Help us evolving such state-of-the-art: propose new attack classes (as some of you are already doing), propose architectural improvements: Dream high! Let us care about making it a reality 
  If you are an end-user: Those attacks are *NOT* complex. Understand and define your threat model, run the available tools and pressure your vendor!
Future
Notes: Vincent -> Rodrigo transition