## Slide 1: DIGITAL LOGIC AND DESIGN
B.Tech(Honours)
CSE(AI/DS)
2nd semester
UTD, CSVTU, Bhilai

## Slide 3: Unit 1-4
Books
R.P. Jain, Modern digital electronics
A.P. Godse, D.A. Godse, Digital Electronics and logic design
Unit 5
Morris Mano, Digital design with verilog HDL
Samir palnitkar, Verilog HDL

## Slide 4: Online PDF books are available in following link ↓
https://www.google.com/url?sa=t&source=web&rct=j&url=https://z-lib.org/&ved=2ahUKEwjdt4zs3oL4AhUxxIsBHTuiBWAQFnoECAUQAQ&usg=AOvVaw317VYZRys6ni4wVkjbg8c0

## Slide 5: CHAPTER – 01 BOOLEAN ALGEBRA
Unit 1

## Slide 6: INTRODUCTION

## Slide 7: INTRODUCTION
Developed by English Mathematician George Boole in between 1815 - 1864.
It is described as an algebra of logic or an algebra of two values i.e True or False.
The term logic means a statement having binary decisions i.e True/Yes or False/No.

## Slide 8: APPLICATION OF BOOLEAN ALGEBRA

## Slide 9: APPLICATION OF BOOLEAN ALGEBRA
It is used to perform the logical operations in digital computer.
In digital computer True represent by ‘1’ (high volt) and False represent by ‘0’ (low volt)
Logical operations are performed by logical operators. The fundamental logical operators are:
1. AND (conjunction)
2. OR (disjunction)
3. NOT (negation/complement)

## Slide 10: AND operator
It performs logical multiplication and denoted by (.) dot.
X Y X.Y
0 0 0
0 1 0
1 0 0
1 1 1

## Slide 11: OR operator
It performs logical addition and denoted by (+) plus.
X Y X+Y
0 0 0
0 1 1
1 0 1
1 1 1

## Slide 12: NOT operator
It performs logical negation and denoted by (-) bar. It operates on single variable.
X X (means complement of x)
0 1
1 0

## Slide 13: Truth Table
Truth table is a table that contains all possible values of logical variables/statements in a Boolean expression.
No. of possible combination =
2n, where n=number of variables used in a Boolean expression.

## Slide 14: Truth Table
The truth table for XY + Z is as follows:
Dec X Y Z XY XY+Z
0 0 0 0 0 0
1 0 0 1 0 1
2 0 1 0 0 0
3 0 1 1 0 1
4 1 0 0 0 0
5 1 0 1 0 1
6 1 1 0 1 1
7 1 1 1 1 1

## Slide 15: Tautology & Fallacy
If the output of Boolean expression is always True or 1 is called Tautology.
If the output of Boolean expression is always False or 0 is called Fallacy.

## Slide 16: Tautology & Fallacy

## Slide 17: Exercise
1. Evaluate the following Boolean expression using Truth Table.
(a) X’Y’+X’Y (b) X’YZ’+XY’
(c) XY’(Z+YZ’)+Z’
2. Verify that P+(PQ)’ is a Tautology.
3. Verify that (X+Y)’=X’Y’

## Slide 18: Implementation
Boolean Algebra applied in computers electronic circuits. These circuits perform Boolean operations and these are called logic circuits or logic gates.

## Slide 19: Logic Gate

## Slide 20: Logic Gate
A gate is an digital circuit which operates on one or more signals and produce single output.
Gates are digital circuits because the input and output signals are denoted by either 1(high voltage) or 0(low voltage).
There are three basic gates and are:
1. AND gate
2. OR gate
3. NOT gate

## Slide 21: AND gate

## Slide 22: AND gate
The AND gate is an electronic circuit that gives a high output (1) only if all its inputs are high.
AND gate takes two or more input signals and produce only one output signal.
Input A | Input B | Output AB
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 23: OR gate

## Slide 24: OR gate
The OR gate is an electronic circuit that gives a high output (1) if one or more of its inputs are high.
OR gate also takes two or more input signals and produce only one output signal.
Input A | Input B | Output A+B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 25: NOT gate

## Slide 26: NOT gate
The NOT gate is an electronic circuit that gives a high output (1) if its input is low .
NOT gate takes only one input signal and produce only one output signal.
The output of NOT gate is complement of its input.
It is also called inverter.
Input A | Output A
0 | 1
1 | 0

## Slide 27
PRACTICAL APPLICATIONS OF LOGIC GATES

## Slide 28
AND Gate
So while going out of the house you set the "Alarm Switch" and if the burglar enters he will set the "Person switch", and tada the alarm will ring.
PRACTICAL APPLICATIONS OF LOGIC GATES

## Slide 29
AND Gate
PRACTICAL APPLICATIONS OF LOGIC GATES
Electronic door will only open if it detects a person and the switch is set to unlocked.
Microwave will only start if the start button is pressed and the door close switch is closed.

## Slide 30
OR Gate
You would of course want your doorbell to ring when someone presses either the front door switch or the back door switch..(nice)
PRACTICAL APPLICATIONS OF LOGIC GATES

## Slide 31
NOT Gate
When the temperature falls below 20c the Not gate will set on the central heating system (cool huh).
PRACTICAL APPLICATIONS OF LOGIC GATES

## Slide 32
NAND, NOR XOR, XNOR GATES

## Slide 33
NAND Gate
Known as a “universal” gate because ANY digital circuit can be implemented with NAND gates alone.

## Slide 34
NAND Gate
NAND
X
Y
Z
X Y Z
0 0 1
0 1 1
1 0 1
1 1 0

## Slide 35
NAND Gate
X
X
F = (X•X)’
= X’+X’
= X’
X
Y
Y
F = ((X•Y)’)’
= (X’+Y’)’
= X’’•Y’’
= X•Y
F = (X’•Y’)’
= X’’+Y’’
= X+Y
X
X
F = X’
X
Y
Y
F X•Y
F = X+Y

## Slide 36
NOR Gate

## Slide 37
NOR Gate
NOR
X
Y
Z
X Y Z
0 0 1
0 1 0
1 0 0
1 1 0

## Slide 38
Exclusive-OR Gate

## Slide 39
Exclusive-OR Gate
X Y Z
XOR
X
Y
Z
0 0 0
0 1 1
1 0 1
1 1 0

## Slide 40
Exclusive-NOR Gate

## Slide 41
Exclusive-NOR Gate
X Y Z
XNOR
X
Y
Z
0 0 1
0 1 0
1 0 0
1 1 1

## Slide 42: Basic Theorem of Boolean Algebra
T1 : Properties of 0
  (a) 0 + A = A (b) 0 A = 0
T2 : Properties of 1
  (a) 1 + A = 1 (b) 1 A = A

## Slide 43: Basic Theorem of Boolean Algebra
T3 : Commutative Law
  (a) A + B = B + A (b) A B = B A
T4 : Associate Law
  (a) (A + B) + C = A + (B + C) (b) (A B) C = A (B C)
T5 : Distributive Law
  (a) A (B + C) = A B + A C (b) A + (B C) = (A + B) (A + C)
  (c) A+A’B = A+B

## Slide 44: Basic Theorem of Boolean Algebra
T6 : Indempotence (Identity ) Law
  (a) A + A = A (b) A A = A
T7 : Absorption (Redundance) Law
  (a) A + A B = A (b) A (A + B) = A

## Slide 45: Basic Theorem of Boolean Algebra
T8 : Complementary Law
  (a) X+X’=1
  (b) X.X’=0
T9 : Involution
  (a) x’’ = x
T10 : De Morgan's Theorem
  (a) (X+Y)’=X’.Y’
  (b) (X.Y)’=X’+Y’

## Slide 46: De Morgan's Theorem

## Slide 47: De Morgan's Theorem 1
Theorem 1 A . B = A + B

## Slide 48: De Morgan's Theorem 1
Theorem 1 A . B = A + B

## Slide 49: De Morgan's Theorem 1
Theorem 1 A . B = A + B

## Slide 50: De Morgan's Theorem 2
Theorem 1 A + B = A . B

## Slide 51: De Morgan's Theorem 2
Theorem 2 A + B = A . B

## Slide 52: De Morgan's Theorem 2
Theorem 2 A + B = A . B

## Slide 53: De Morgan's Theorem 2
Theorem 2 A + B = A . B

## Slide 54: Thank You