## Slide 1: Binary Addition & Subtraction

## Slide 2: Binary Addition
A | B | OUT
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 10

## Slide 3: Example
101 + 101

## Slide 4: Example
10001 + 11101

## Slide 5: Example
10111 + 110001

## Slide 6: Binary Subtraction
A | B | OUT
0 | 0 | 0
1 | 0 | 1
0 | 1 | 1(Borrow 1 from next digit)
1 | 1 | 0

## Slide 7: Example
1 0 1 0 – 101

## Slide 8: Example
110101 – 100101

## Slide 9: Example
101011 – 111001

## Slide 10: What about this?
101 - 1010

## Slide 11: Negative Number Representation
-ve sign (Sign Magnitude)
1’s compliment
2’s compliment

## Slide 12: Example

## Slide 13: Questions
1011011 − 10010 = ?
1010110 − 101010 = ?
1000101 − 101100 = ?
100010110 − 1111010 = ?
101101 − 100111 = ?
1110110 − 1010111 = ?

## Slide 14: Questions
1011011 − 10010 = 1001001
1010110 − 101010 = 101100
1000101 − 101100 = 11001
100010110 − 1111010 = 10011100
101101 − 100111 = 110
1110110 − 1010111 = 11111

## Slide 15: Limitations of Signed Magnitude
For 0, there are two representations: -0 and +0 which should not be the case as 0 is neither –ve nor +ve.
Out of 2^n bits for representation, we are able to utilize only 2^{n-1} bits.
Numbers are not in cyclic order i.e. After the largest number (in this, for example, +7) the next number is not the least number (in this, for example, +0).

## Slide 16: Contd.
For negative numbers signed extension does not work.

## Slide 17: Limitations of 1’s Compliment
For 0, there are two representations: -0 and +0 which should not be the case as 0 is neither –ve nor +ve.
Out of 2^n bits for representation, we are able to utilize only 2^{n-1} bits.

## Slide 18: Signed Extension in 1’s Compliment
You need to add 0/1 in the MSB.

## Slide 19: Homework
Design a circuit for 4-bit addition and subtraction of 2 binary numbers. A control bit will decide whether addition or subtraction needs to be performed. Consider an additional bit for signed representation.
Repeat the above using 1’s compliment method.
Repeat the above using 2’s compliment method.

## Slide 20: Exception 1
0 = 00000000 (twos complement)
Bitwise complement = 11111111
Add 1 to LSB + 1
Result 100000000
Overflow is ignored, so:
- 0 = 0

## Slide 21: Exception 2: bit pattern 1{0}{1,n}
-128 = 10000000 (twos complement)
Bitwise complement = 01111111
Add 1 to LSB + 1
Result 10000000
So:
-(-128) = -128 X
Monitor MSB (sign bit)
It should change during negation

## Slide 22: Overflow
If two numbers are added, and they are both positive or both negative, then overflow occurs if and only if the result has the opposite sign.

## Slide 23: Multiplication Basics
0 × 0 = 0
0 × 1 = 0
1 × 0 = 0
1 × 1 = 1

## Slide 24: Example 1
Solve 1010 × 101

## Slide 25: Example 1
Solve 1010 × 101
1010
101
-------
1010
0000X
1010XX
----------
110010

## Slide 26: Example 2
Solve 1011.01 × 110.1

## Slide 27: Example 2
Solve 1011.01 × 110.1
1011.01
110.1
------------
101101
000000X
101101XX
101101XXX
---------------
1001001001

## Slide 28: Self Practice
Solve 10001 x 111
Solve 10101 x 110
Solve 11111 x 10000

## Slide 29: Multiplication

## Slide 30: Multiplication of –ve numbers
What if you multiply 1001 (-7) and 1101 (-3)?

## Slide 31: Conversion to +ve number and decide sign
What if you multiply 1001 (-7) and 1101 (-3)?

## Slide 32: Sign-Extend Method (2’s Compliment Multiplication)
What if you multiply 1001 (-7) and 1101 (-3)?

## Slide 33: Motivation for Booth’s Algorithm
The important thing to note about two’s complement multiplication is that the number of additions/subtractions that we do is identical to the number of 1’s in the multiplier.
So, a multiplier with ten 1’s will require ten addition/subtraction operations, whereas a multipler with only a single 1 will only require one addition/subtraction operation.

## Slide 34: Background
Number 5 in binary using 4 bits
0101
Number -5 in binary using 4 bits 2’s compliment
1011
How to justify the above using place value logic?

## Slide 35: Contd.
2’s compliment of 5: 1011
Sometimes the –ve 1 is represented as one bar.
We take one bar to simply mean -1. We will call this balanced ternary representation.
Thus 7 represented as 0111 can also be represented as 100one bar.
-2^3 | 2^2 | 2^1 | 2^0
1 | 0 | 1 | 1

## Slide 36: Contd.
How does this help?
0111 for each 1 we need to shift and add while for each 0 we need only to shift. Since the shift calculators were fast, it was better to have multiple zeros than ones.

## Slide 37: Booth’s Algorithm
Booth algorithm gives a procedure for multiplying binary integers in signed 2’s complement representation in efficient way, i.e., less number of additions/subtractions required.
It operates on the fact that strings of 0’s in the multiplier require no addition but just shifting.
Also, a string of 1's in a multiplier bit weight 2k to weight 2m that can be considered as 2k+ 1 - 2m.

## Slide 38: Contd.
As in all multiplication schemes, booth algorithm requires examination of the multiplier bits and shifting of the partial product. Prior to the shifting, the multiplicand may be added to the partial product, subtracted from the partial product, or left unchanged according to following rules:
1. The multiplicand is subtracted from the partial product upon encountering the first least significant 1 in a string of 1’s in the multiplier
2. The multiplicand is added to the partial product upon encountering the first 0 (provided that there was a previous ‘1’) in a string of 0’s in the multiplier.
3. The partial product does not change when the multiplier bit is identical to the previous multiplier bit.

## Slide 39: Arithmetic Shift (ashr)
Right Shift
Left Shift

## Slide 40: Flowchart

## Slide 41: Example
A numerical example of booth’s algorithm is shown below for n = 4. It shows the step by step multiplication of -5 and -7.
-6 x -7
BR QR
Multiplicand Multiplier

## Slide 42: Execution
BR = -5 = 1011,
BR' = 0100, <-- 1's Complement (change the values 0 to 1 and 1 to 0)
BR'+1 = 0101 <-- 2's Complement (add 1 to the Binary value obtained after 1's compliment)
QR = -7 = 1001 <-- 2's Complement of 0111 (7 = 0111 in Binary)
The explanation of first step is as follows:
  AC = 0000,
  QR = 1001,
  Qn+1 = 0,
  SC = 4

## Slide 43: Contd.
  Qn Qn+1 = 10
  So, we do AC + (BR)'+1, which gives AC = 0101
  On right shifting AC and QR, we get AC = 0010, QR = 1100 and Qn+1 = 1

## Slide 44: Contd.
OPERATION | AC | QR | Qn+1 | SC
 | 0000 | 1001 | 0 | 4
AC + BR’ + 1 | 0101 | 1001 | 0 | 
ASHR | 0010 | 1100 | 1 | 3
AC + BR | 1101 | 1100 | 1 | 
ASHR | 1110 | 1110 | 0 | 2
ASHR | 1111 | 0111 | 0 | 1
AC + BR’ + 1 | 0100 | 0111 | 0 | 
ASHR | 0010 | 0011 | 1 | 0

## Slide 45: Solution
Product = AC QR
Product = 0010 0011 = 35

## Slide 46: Example 2
-4 X -5
OPERATION | AC | QR | Qn+1 | SC

## Slide 47: Example 2
-4 X -5
OPERATION | AC | QR | Qn+1 | SC
 | 0000 | 1011 | 0 | 4
AC + BR’ + 1 | 0100 | 1011 | 0 | 
ASHR | 0010 | 0101 | 1 | 3
ASHR | 0001 | 0010 | 1 | 2
AC + BR | 1101 | 0010 | 1 | 
ASHR | 1110 | 1001 | 0 | 1
AC + BR’ + 1 | 0010 | 1001 | 0 | 
ASHR | 0001 | 0100 | 1 | 0

## Slide 48: Binary Division
A | B | A/B
0 | 0 | Meaningless
0 | 1 | 0
1 | 0 | Meaningless
1 | 1 | 1

## Slide 49: Example 1
(01111100)2 / (0010)2

## Slide 50: Solution 1
(01111100)2 = (1111100)2 = 12410
(0010)2 = (10)2 = 210
You will get the resultant value as 62 when you divide 124 by 2.
So the binary equivalent of 62 is (111110)2
.(111110)2 = 6210

## Slide 51: Solution 2
By Long Division
1111100
10

## Slide 52: Solve
Solve using the long division method: 101101 ÷ 101

## Slide 53: 2’s Compliment Division (repeated subtraction)
Step 1: Check for signs. Based on sign, decide the sign of the quotient.
Step 2: Subtract the divisor from the dividend using 2’s compliment addition (remember that the final carries are discarded).
Step 3: Repeat until you get zero remainder or a value less than the divisor’s magnitude.

## Slide 54: Example 1
dividend 1111100
divisor 0000100
2’s compliment 1111100
Repeat 2’s compliments addition till termination

## Slide 55: Contd.
dividend 1111100
2’s compliment 1111110
1111010
1111000
1110110
1110100
1110010
1110000
1101110
1010000
1001110
1001100
1001010
1001000
1000110
1000100
1000010
1000000
0111110
0111100
0111010
0111000