## Slide 1: CACHE MEMORY AND VIRTUAL MEMORY
PRESENTED BY Madhurima Rawat ROLL NO- DATASCIENCE(CSE)
Chhattisgarh Swami
Vivekananda Technical
University

## Slide 2: Cache Memory
Cache memory is a Random Access Memory.
Cache Memory is defined as a very high speed memory that is used in computer system to compensate the seed differential between the main memory access time and processor logic.
A very high speed memory called a cache is used to increase the speed of processing by making current programs and data available to the CPU at a rapid rate. It is place between the CPU and the main memory.

## Slide 3: WHY WE REQUIRE CACHE MEMORY
The references to memory at any given interval of time tend to be confined within a few localized areas in memory known as the property of locality of reference.
The cache memory access time is less than the access time of main memory by a factor of 5 to 10. The cache is the fastest component in the memory hierarchy and approaches the speed of CPU components.
The basic operation of the cache is as follows. When the CPU needs to access memory, the cache is examined. If the word is found in the cache, it is read from the fast memory. If the word addressed by the CPU is not found in the cache, the main memory is accessed to read the word.

## Slide 4: USE OF CACHE MEMORY
The performance of cache memory is frequently measured in terms of a quantity called hit ratio.
When the CPU refers to memory and finds the word in cache, it is said to produce a hit.
If the word is not found in cache, it is in main memory and it counts as a miss. The ratio of the number of hits divided by the total CPU references to memory is the hit ratio.
The average memory access time of a computer system can be improved considerably by use of a cache. If the hit ratio is high enough so that most of the time the CPU accesses the cache instead of main memory, the average access time is closer to the access time of the fast cache memory.

## Slide 5: CACHE MAPPING
The basic characteristic of cache memory is its fast access time. Therefore, very little or no time must be wasted when searching for words in the cache. The transformation of data from main memory to cache memory is referred to as a mapping process.
Three types of mapping procedures are of practical interest when considering the organization of cache memory.
Direct mapping
Associative mapping/ fully associative mapping
3. Set-associative mapping/ k-way associative mapping

## Slide 6: VIRTUAL MEMORY
Virtual Memory is a concept used in some large computer system that permit the user to construct programs as though a large space were available, equal to the totality of auxiliary memory.
Each address that is referenced by the CPU goes through an address mapping from the so-called virtual address to a physical address in main memory.
A virtual memory system provides a mechanism for translating program generated addresses into correct main memory locations. This is done dynamically, while programs are being executed in the CPU.
. It gives the programmer the illusion that they have a very large memory at this disposal even though the computer actually has a relatively small main memory.

## Slide 7: HOW IT IS DONE?
Say, for a PC with 256 MB RAM & 40 GB hard disk, the auxiliary memory is 40 GB, but the main memory is 256 Megabyte, but in virtual memory concept, the user shall have a feeling of 40Gbyte main memory.
A virtual memory system provides a mechanism for translating program generated addresses into correct main memory locations.
This done dynamically, while programs are being executed in the CPU. The translation or mapping of virtual address to physical address is handled by the hardware by the means of a mapping table.
The address used by the programmer is called virtual address.

## Slide 8: VIRTUAL ADDRESS
The address in the main memory is called physical address. For the specification cited above, the address space is of 40X10 the power 12 and the memory space is of 256X 10 to the power 6 words. The memory table for mapping a virtual address is given below:

## Slide 9: ADVANTAGES
Allowing users to operate multiple applications at the same time or applications that are larger than the main memory.
Freeing applications from having to compete for shared memory space and allowing multiple applications to run at the same time.
Improving efficiency and speed by allowing more processes to sit in virtual memory.
Increasing the amount of memory available by working outside the limits of a computer's physical main memory space.
Optimizing central processing unit (CPU) usage.

## Slide 10
THANK YOU FOR LISTENING TO MY PRESENTATION
ANY QUESTIONS