## Slide 1: Case Study: Autonomous Warehouse Robot

## Slide 2: Reactive Architecture
Reactive control architectures are based on immediate responses to stimuli from the environment.
They do not involve complex reasoning or planning but rely on sensors to make quick decisions.

## Slide 3: Implementation
Sensors : Ultrasonic sensors for obstacle detection, and infrared sensors for line-following.
Behavior : The robot is programmed with a set of simple behaviors (e.g., avoid obstacles, follow a path).
Example: If the robot detects an obstacle in its path, it immediately alters its trajectory to navigate around it without analyzing the overall route or planning ahead.

## Slide 4: Advantages :
Fast response times due to direct sensor feedback.
Simplicity in design and implementation.

## Slide 5: Limitations
Cannot handle complex tasks or plan for future goals.
Performance can degrade in dynamic environments with multiple obstacles.

## Slide 6: Deliberative Architecture
Deliberative architectures use planning and reasoning to make decisions.
They maintain a model of the environment and can evaluate future states to choose optimal actions.

## Slide 7: Implementation
Sensors : Cameras for visual recognition, GPS for localization, and LiDAR for mapping.
Planning : The robot creates a map of the warehouse and plans a route to reach the designated inventory shelf.
Example : Before moving, the robot assesses the entire environment, calculates the best path, considers potential obstacles, and develops a detailed plan.

## Slide 8: Advantages and Limitation
Advantages:
Capable of handling complex tasks and long-term goals.
Better suited for environments where prior knowledge and planning are essential.
Limitations:
Slower response times due to the planning phase.
More complex algorithms require significant computational resources.

## Slide 9: Hybrid Architecture
Hybrid architectures combine elements of both reactive and deliberative systems, leveraging the strengths of each approach.
They typically use a layered approach where high-level planning coexists with low-level reactive behaviors

## Slide 10: Implementation
Sensors : The same set of sensors used in both previous architectures.
Planning and Control : The robot builds a map of the warehouse and plans its route, but it also maintains reactive behaviors to avoid obstacles in real time.
Example : While navigating to a shelf, the robot follows a planned route. If it encounters an unexpected obstacle, it temporarily switches to a reactive mode to navigate around it, then returns to its planned path once the obstacle is cleared.

## Slide 11: Advantage and limitation
Advantages:
Balances the speed of reactive systems with the sophistication of deliberative planning.
More robust in dynamic environments, as it can adapt quickly while still pursuing long-term goals.
Limitations :
Increased complexity in the architecture and integration of components.
Potential for conflicts between reactive and deliberative layers if not designed properly.

## Slide 12: Conclusion
A reactive architecture would allow the robot to quickly respond to obstacles but could lead to inefficient routes and missed inventory tasks.
A deliberative architecture would enable more efficient path planning but might struggle in dynamic scenarios where quick reactions are needed.
A hybrid architecture offers the best of both worlds, enabling the robot to plan routes while also reacting to immediate obstacles, making it ideal for the unpredictable warehouse environment.