## Slide 1: BSD CARD AN INSIDE LOOK
LCC Fusion Project Understanding the Hardware
Behind Block Detection
Pat Fleming
Email: PatFlemingHTC@Gmail.com
Notes: (voice: Nelson) Welcome back to the LCC Fusion Project series. Earlier, we looked at how the Block Breakout Board organizes the wiring for each block. Now we’re stepping into the part of the system that decides what’s actually happening in those blocks.
(pause: 0.8)
(voice: Harrison) Today we’re looking at the BSD Card, the Block Short Detection Card. And this card does more than occupancy. It monitors four blocks, determines whether each one is clear, occupied, or shorted, and then reports those results to the Node Card over I2C.
(pause: 0.8)
(voice: Nelson) And this card reacts to shorts too, right?
(pause: 0.8)
(voice: Harrison) Exactly. When a short happens, the BSD Card cuts power, waits, and restores it. It’s the first responder — not just a detector.
(pause: 0.8)
(voice: Nelson) And those short events can drive alerts, sounds, or even voice announcements, thanks to Fusion’s LCC-based automation.

## Slide 2: Recap: What the Block Breakout Board Provides
What We Learned Last Time
Organizes feeder wiring for 4 blocks
Sends block sense lines to BSD Card
Supports snubber/trickle options
No logic — wiring only
Shared across BOD and BSD systems
Notes: (voice: Nelson) Before we dive into the BSD, let’s recap what the Block Breakout Board does.
(pause: 0.8)
(voice: Harrison) It’s just the wiring layer. It organizes the feeders for four blocks and brings those lines cleanly to the BSD Card. There’s no logic — just neat, reliable wiring.
(pause: 0.8)
(voice: Nelson) So the BSD Card builds on top of that foundation.
(pause: 0.8)
(voice: Harrison) Exactly. The Breakout handles the wires; the BSD handles the decisions.

## Slide 3: Where the BSD Card Fits & What It Does
Its Role in Block & Short Detection
Handles 4 blocks
Determines clear / occupied / short
ESP32 analyzes current and protects blocks
Sends states to Node Card via I2C
Node Card publishes LCC events
Notes: (voice: Nelson) So where does the BSD Card actually sit in the Fusion system? What is its job in the bigger picture?
(pause: 0.8)
(voice: Harrison) The BSD Card sits right above the Block Breakout Board. The Breakout Board brings in the four block feeder lines, and those lines go straight into the BSD Card’s sensing and protection circuitry. From there, the BSD Card’s ESP32 takes over — it reads each block’s digital current level, applies filtering, and decides whether each block is clear, occupied, or shorted.
(pause: 0.8)
(voice: Nelson) So the BSD Card is doing the electrical interpretation before the Node Card ever sees anything.
(pause: 0.8)
(voice: Harrison) Exactly. The ESP32 handles all the local processing — current measurement, occupancy logic, short detection, debounce filtering, state tracking, and even the automatic short-recovery cycle where it turns the block off, waits, and restores it. All of that happens right on the BSD Card, close to the blocks where the electrical behavior is happening.
(pause: 0.8)
(voice: Nelson) And once it figures all of that out, how does the rest of Fusion learn about it?
(pause: 0.8)
(voice: Harrison) The BSD Card does not publish LCC events directly. Instead, it sends simple, clean I2C text commands to the Node Card. Those commands say, “Block 1 is clear,” or “Block 3 is occupied,” or “Block 2 is shorted.” The Node Card takes those results and publishes the official LCC events onto the kanbus.
(pause: 0.8)

## Slide 4: Where the BSD Card Fits & What It Does
Its Role in Block & Short Detection
Handles 4 blocks
Determines clear / occupied / short
ESP32 analyzes current and protects blocks
Sends states to Node Card via I2C
Node Card publishes LCC events
Notes: (voice: Nelson) Why doesn’t the BSD Card publish the LCC events itself?
(pause: 0.8)
(voice: Harrison) Because Fusion uses a three-tier architecture. The BSD Card specializes in detection and protection. The Node Card specializes in event publishing and layout logic. This keeps each card simple and reliable — and it keeps LCC messaging centralized so logic rules, signals, and automation all behave consistently.
(pause: 0.8)
(voice: Nelson) So the BSD Card is the sensor and protector… and the Node Card is the communicator and decision-maker.
(pause: 0.8)
(voice: Harrison) Exactly. The BSD handles the electrical truth of the block. The Node Card handles the LCC automation. That’s why the BSD fits perfectly in the middle — between clean wiring below it and system-wide logic above it.
(pause: 0.8)
(voice: Nelson) And because it reports interpreted states — not raw values — everything downstream stays simple and reliable.
(pause: 0.8)
(voice: Harrison) Right. No noise, no raw signals, no filtering on the Node side. Just clear, stable block states the rest of the system can trust.

## Slide 5: Why Use BSD Instead of BOD?
BSD adds short detection + auto-reset
Designed for high-importance blocks
BOD = coverage; BSD = protection
BSD handles 4 blocks;
BOD handles 8
Short events can trigger operator alerts
Notes: (voice: Nelson) Why do we need a BSD Card when we already have a BOD Card? Aren’t they both just block detectors?
(pause: 0.8)
(voice: Harrison) They are both detectors, but they’re designed for very different jobs. The BOD Card is about coverage — detecting occupancy on a lot of blocks at a low cost. It’s perfect for staging yards, sidings, and anywhere you want broad visibility without a lot of expense.
(pause: 0.8)
(voice: Nelson) So what makes the BSD Card different?
(pause: 0.8)
(voice: Harrison) The BSD Card is designed for high-importance blocks — places where shorts matter: mainlines, crossovers, yard throats, interlockings, and station approaches. Those are the blocks where a short can disrupt traffic or shut down an entire district.
(pause: 0.8)
(voice: Nelson) And the BSD handles the short locally instead of letting the DCC power supply trip?
(pause: 0.8)
(voice: Harrison) Exactly. The BSD isn’t just detecting. It’s protecting. It shuts down the block the moment it detects a short, waits, then restores power to see if the short has cleared. That keeps the rest of the layout running, instead of everything going dark.
(pause: 0.8)
(voice: Nelson) So BOD is “lots of blocks cheaply,” and BSD is “critical blocks with protection.”
(pause: 0.8)
(voice: Harrison) Right. The BOD Card gives you 8 blocks per card. The BSD gives you 4 blocks, but with solid-state power switch control, digital current sensing, short recovery, and local protection. Completely different tool, different purpose.
(pause: 0.8)

## Slide 6: Why Use BSD Instead of BOD?
BSD adds short detection + auto-reset
Designed for high-importance blocks
BOD = coverage; BSD = protection
BSD handles 4 blocks;
BOD handles 8
Short events can trigger operator alerts
Notes: (voice: Nelson) Where does automation fit into this? What happens when the BSD detects a short?
(pause: 0.8)
(voice: Harrison) That’s where Fusion shines. The moment the BSD flags a short, the Node Card publishes the short event. Many possible results could occur next; Signals drop to red, routes lock out, logic pauses movement, and the dispatcher or operator can get a voice alert telling them exactly which block has the issue.
(pause: 0.8)
(voice: Nelson) That’s a huge improvement over a DCC power supply trip where everyone starts guessing what happened.
(pause: 0.8)
(voice: Harrison) Exactly. With a DCC power supply trip, the whole district goes down and you have no idea why. With the BSD, you know which block, why, when, and what the card is doing about it. It’s immediate, localized, and completely visible.
(pause: 0.8)
(voice: Nelson) So the BSD isn’t just a fancy detector — it’s a reliability tool.
(pause: 0.8)
(voice: Harrison) That’s exactly it. Use the BOD when you want coverage. Use the BSD when the block is important, when shorts need to be handled instantly, and when the rest of the layout must stay operational.
(pause: 0.8)
(voice: Nelson) Which means most mainlines and interlockings should use BSD, and everything else can rely on BOD.
(pause: 0.8)
(voice: Harrison) Perfect summary. And that’s why both cards exist — each one solves a different problem, and together they give you full visibility and full protection across the entire layout.

## Slide 7: Top View Overview
Solid-state power switch power stages (4 blocks)
Current sensors
Short-protection circuits
Occupied + Short LEDs
ESP32 module
Node Bus, I2C address, EEPROM
Notes: (voice: Nelson) Walk me through the top of the BSD Card. What am I actually looking at here?
(pause: 0.8)
(voice: Harrison) Everything on the top is organized by block subsystem. Each of the four blocks has its own cluster of parts — the solid-state power switches (MOSFET) that control power, the current sensor that measures draw, and the short-protection components that protect the block. You can literally follow the electrical path from the connector into the solid-state power switch stage, through the sensor, and into the ESP32’s inputs.
(pause: 0.8)
(voice: Nelson) And those solid-state power switches — what job are they doing?
(pause: 0.8)
(voice: Harrison) They’re the switches that actually control block power. The firmware can turn the block on, turn it off, or cycle it during a short-recovery sequence. By putting a solid-state power switch pair on each block, the BSD Card can isolate a short locally without shutting down the entire district.
(pause: 0.8)
(voice: Nelson) What about the sensors? How do they feed information back?
(pause: 0.8)
(voice: Harrison) Each block has a digital current sensor, and that’s one of the key features of this card. The ESP32 reads those values directly, digitally, and uses them to decide whether the block is clear, occupied, or shorted. The sensors are grouped tightly with their solid-state power switch stage so the readings stay accurate and noise stays low.
(pause: 0.8)
(voice: Nelson) I see some other components in each cluster too — the protection parts?
(pause: 0.8)

## Slide 8: Top View Overview
MOSFET power stages (4 blocks)
Current sensors
Short-protection circuits
Occupied + Short LEDs
ESP32 module
Node Bus, I2C address, EEPROM
Notes: (voice: Harrison) Right. Each block has its own protection network — resistors, capacitors, and filtering components — that make the readings stable. Those parts help smooth out the signal and prevent false short detections. The layout is intentional: everything that belongs to Block 1 is together, Block 2 is together, and so on.
(pause: 0.8)
(voice: Nelson) And the ESP32 is all the way over on the right side?
(pause: 0.8)
(voice: Harrison) Yes. The ESP32 is physically separated from the high-current areas to keep the digital side clean. It reads the sensor values, applies filtering, decides the state, handles short recovery, and issues I2C updates to the Node Card. It’s the control center for the entire board.
(pause: 0.8)
(voice: Nelson) Now, those LEDs — that seems straightforward, but they’re pretty important when you’re testing, right?
(pause: 0.8)
(voice: Harrison) Absolutely. Each block has two LEDs: one for occupied, one for shorted. They come straight from the firmware decisions. If you see the occupied LED, you know the current is within your configured range. If you see the short LED, the block is being shut down and protected. They’re the quickest diagnostic tools on the card.
(pause: 0.8)
(voice: Nelson) So everything on the top is arranged for clarity — electrical path on the left, intelligence on the right, and diagnostics right in front of you.
(pause: 0.8)
(voice: Harrison) Exactly. It’s designed so builders can trace the path visually, and operators can glance at it and instantly understand what’s happening. Clean layout, easy debugging, and purpose-built for reliability.

## Slide 9: Bottom View Overview
Component-free bottom
Silkscreen orientation
Block numbering
Node Bus alignment
Card ID + version
Notes: (voice: Nelson) When we flip the card over, the bottom still doesn’t have any components. So what’s the purpose of the bottom silkscreen on the BSD Card?
(pause: 0.8)
(voice: Harrison) The bottom side is there for identification and basic power information. You’ll see the card name, the version, and a brief note about how the card is meant to be used — specifically that it works with the Block Breakout Board.
(pause: 0.8)
(voice: Nelson) And you have a power reminder down here too?
(pause: 0.8)
(voice: Harrison) Yes. There’s a simple line showing the DCC power supply output maximum per block. This is based on using a CAT6 network cable and the limits of its 23 gauge wires. It’s not meant to be exact engineering data — just a quick reference so builders know what power limit the card expects.
(pause: 0.8)
(voice: Nelson) So the bottom isn’t part of the circuitry — it’s part of the documentation.
(pause: 0.8)
(voice: Harrison) Exactly. The electronics are all on top. The bottom carries the identity, the version, the important notes about power, and the reminder of what this card connects to. It’s the quick-reference information a builder needs when picking up the card later.

## Slide 10: How Block Detection & Short Protection Work
Firmware reads digital current
Compares to occupancy range
Short = high-current spike
Controls MOSFET block power
Auto-reset after short
Reports state to Node Card
Notes: (voice: Nelson) How does the BSD actually decide the block state? What’s happening inside the firmware?
(pause: 0.8)
(voice: Harrison) The firmware reads the digital current value coming from each block. It samples that value many times a second and applies filtering so short flickers don’t cause false triggers. Once the signal is clean, it compares the current to the ranges you configured in the Admin View.
(pause: 0.8)
(voice: Nelson) So the occupancy decision is based entirely on that configured range?
(pause: 0.8)
(voice: Harrison) Exactly. If the current rises above the baseline and stays inside your occupancy range, the firmware marks the block as occupied. That’s how it handles different locomotives — some draw more, some draw less — the range lets you tune it.
(pause: 0.8)
(voice: Nelson) And what about shorts? How does it recognize those?
(pause: 0.8)
(voice: Harrison) Shorts behave very differently. Instead of a steady moderate draw, the current jumps sharply. The firmware watches for those spikes, and if the reading crosses the short threshold — and it stays there long enough to rule out noise — the block is marked as shorted.
(pause: 0.8)
(voice: Nelson) So the BSD is looking for both the amount of current and the behavior of that current?
(pause: 0.8)

## Slide 11: How Block Detection & Short Protection Work
Firmware reads digital current
Compares to occupancy range
Short = high-current spike
Controls a solid-state power switch per block
Auto-reset after short
Reports state to Node Card
Notes: (voice: Harrison) Right. Occupancy is “steady and moderate.” A short is “instant jump and very high.” Clear is when the current falls back to its baseline value.
(pause: 0.8)
(voice: Nelson) And it controls block power too, correct?
(pause: 0.8)
(voice: Harrison) Yes. The moment the firmware detects a short, it turns the block off using the solid-state power switch stage. Then it waits briefly — just long enough for the rails to settle — and restores power to see if the short has cleared. If it hasn’t cleared, the firmware repeats the cycle. If the short has cleared, the block goes right back to normal operation.
(pause: 0.8)
(voice: Nelson) So the BSD isn’t just reporting state — it’s actively protecting the block.
(pause: 0.8)
(voice: Harrison) Exactly. It handles detection, protection, filtering, and recovery right on the card, and then reports the final, stable block state to the Node Card over I2C.

## Slide 12: Occupied vs Shorted Logic
Occupied = moderate current
Short = high-current spike
Clear = baseline
ESP32 filters noise
Decisions remain stable
Notes: (voice: Nelson) How does it separate occupied from short?
(pause: 0.8) (voice: Harrison) Level and behavior. Occupied is steady moderate current. Short is a sharp spike. The ESP32 applies filtering to avoid false triggers.

## Slide 13: Why Not Let the Node Card Handle Everything?
High-current sensing belongs at the block
Offloads work from Node Card
Fusion uses edge computing
Distributed responsibilities
Three-tier architecture
Notes: (voice: Nelson) Why not just let the Node Card do all of this? Why not plug the block wiring directly into the Node Card and have it handle detection and shorts itself?
(pause: 0.8)
(voice: Harrison) Because that would break the Fusion 3-tier architecture. Block sensing and short protection involve high current, fast spikes, and instant reaction times. If we combined all of that with the Node Card’s logic, we’d overload the components on the Node Card and blur the roles of the system.
(pause: 0.8)
(voice: Nelson) So the architecture itself is what prevents us from merging them?
(pause: 0.8)
(voice: Harrison) Exactly. The BSD Card is part of the edge tier — close to the rails, handling electrical work. The Node Card sits in the logic tier — running automation, events, and configuration. If you tried to put BSD-level sensing and protection on the Node Card, you'd mix high-current electronics with delicate logic, add electrical noise, and make the Node Card much harder to design and maintain.
(pause: 0.8)
(voice: Nelson) And this would make upgrades more difficult too, right?
(pause: 0.8)
(voice: Harrison) Absolutely. Separating the tiers means you can upgrade or replace the BSD Card without touching the Node Card firmware, and vice-versa. If everything were merged, an improvement in block detection would force a whole new Node Card design, new firmware, new testing — the modularity would be gone.
(pause: 0.8)
(voice: Nelson) So splitting the responsibilities keeps the Node Card from getting overloaded?
(pause: 0.8)
(voice: Harrison) Yes. The Node Card isn’t built to monitor raw current spikes or control four block power channels. Its components aren’t sized for that, and the firmware would get bogged down trying to manage real-time short protection. By keeping the BSD as a separate card, we preserve performance, responsiveness, and reliability.
(pause: 0.8)
(voice: Nelson) And how does this help with scaling the system?
(pause: 0.8)
(voice: Harrison) It makes scaling easy. You can add more BSD Cards without adding more Node Cards. That means more protected blocks — without increasing the number of processors, logic engines, or configurations the layout has to manage. It keeps the system clean and predictable as it grows.
(pause: 0.8)
(voice: Nelson) So the BSD stays at the edge, the Node Card stays in the logic tier, and that’s what keeps Fusion modular, maintainable, and scalable.
(pause: 0.8)
(voice: Harrison) Exactly. Dedicated cards doing dedicated jobs — that’s the heart of the Fusion architecture.

## Slide 14: Why Not Let the Node Card Handle Everything?
High-current sensing belongs at the block
Offloads work from Node Card
Fusion uses edge computing
Distributed responsibilities
Three-tier architecture
Notes: (voice: Harrison) It does — big time. Because each BSD Card handles all of its own block sensing and protection, you can add up to 16 BSD Cards as you want without adding more LCC Nodes, for a total of 64 blocks. You’re scaling the block detection system horizontally, but the LCC network stays simple and uncluttered.
(pause: 0.8)
(voice: Nelson) So we get more blocks, more protection, more coverage— but without increasing the number of LCC devices on the network.
(pause: 0.8)
(voice: Harrison) Right. Every BSD Card handles its own electrical work, and the Node Card only receives the final, clean block states. That’s what keeps the whole Fusion system scalable and easy to manage.
(pause: 0.8)
(voice: Nelson) So keeping detection and protection local means the Node Card stays efficient, we avoid running heavy power up to it, and we can grow the system without exploding the number of nodes.
(pause: 0.8)
(voice: Harrison) Exactly. That’s the whole idea: local electrical work, centralized logic, and unlimited scalability without extra nodes.
This is what is called a Scale Up model vs a multi-node scale out model. Fusion supports both models.

## Slide 15: Connectors & Interfaces
J1: 4 block inputs
Node Bus edge connector
I2C address switch + EEPROM
DCC power supply input (required)
Optional I2C display
Notes: (voice: Nelson) Where does everything plug in on the BSD Card? How does all of this connect together?
(pause: 0.8)
(voice: Harrison) Everything starts with J1 — that’s the connector that brings in the four block lines from the Block Breakout Board. Each block comes in on its own pair, and from there it goes straight into its solid-state power switch stage and current sensor on the BSD Card.
(pause: 0.8)
(voice: Nelson) And the Node Bus edge connector — that’s the standard Fusion interface, right?
(pause: 0.8)
(voice: Harrison) Exactly. The Node Bus supplies the BSD Card with logic power and the I2C communication lines. It does not carry block power — just the 3.3-volt logic rail and the digital communication the ESP32 uses to report block states to the Node Card.
(pause: 0.8)
(voice: Nelson) So the Node Bus is low-power logic only, not track power.
(pause: 0.8)
(voice: Harrison) Correct. That keeps the Node Bus clean, light, and noise-free. All the heavy power work is handled through the DCC power supply input, which is the next connector.
(pause: 0.8)
(voice: Nelson) Tell me more about the DCC power supply input. Why is that connection mandatory?
(pause: 0.8)

## Slide 16: Connectors & Interfaces
J1: 4 block inputs
Node Bus edge connector
I2C address switch + EEPROM
DCC power supply input (required)
Optional I2C display
Notes: (voice: Harrison) Because the BSD Card is powering four entire track blocks. The solid-state power switch stages switch block power on and off, and the current sensors measure the draw — so the BSD must get its track power directly from a DCC power supply feed. The Node Bus can’t supply that kind of current, so the DCC power supply connection is required.
(pause: 0.8)
(voice: Nelson) And what about those configuration parts — the switch and the EEPROM?
(pause: 0.8)
(voice: Harrison) The I2C address switch tells the Node Card which BSD Card this is, especially when you have more than one in the cluster. And the EEPROM identifies the card type, so the Node Card immediately knows it’s talking to a BSD Card and not something else. That keeps addressing clean and avoids conflicts.
(pause: 0.8)
(voice: Nelson) So every connector has a clear job: J1 brings in the blocks, the Node Bus brings in logic and comms, and the DCC power supply input brings in power.
(pause: 0.8)
(voice: Harrison) Exactly. By separating the roles — logic power, block power, and block wiring — the BSD Card stays modular, reliable, and easy to integrate into any Fusion configuration.

## Slide 17: Testing the BSD Card
Run Node Card self-test
Node Bus + DCC power supply
ESP32 boots
Occupied test with small load
Short test with safe momentary short
I2C reports to Node Card
Events visible in serial output
Notes: (voice: Nelson) Once someone builds the BSD Card, how do they test it? Where should they start?
(pause: 0.8)
(voice: Harrison) Start with the Node Card’s self-test. That’s always step one. When you run the self-test, the Node Card scans the I2C bus and confirms that a BSD Card is connected at the expected address, that the EEPROM is readable, and that the card identifies itself correctly. If the self-test passes, you know the BSD Card’s communication and identification hardware are good.
(pause: 0.8)
(voice: Nelson) So the self-test confirms the wiring and the I2C activity before we ever put power to the blocks.
(pause: 0.8)
(voice: Harrison) Exactly. If the Node Card can’t find the BSD Card during the self-test, nothing else will work — so verifying that first saves a lot of time.
(pause: 0.8)
(voice: Nelson) Okay, so once the self-test sees the BSD Card, what’s next?
(pause: 0.8)
(voice: Harrison) Next, connect both power sources: the Node Bus for the ESP32 and logic, and the DCC power supply input for the block power. You need both, because without the DCC power supply, the solid-state power switch stages and sensors can’t operate.
(pause: 0.8)
(voice: Nelson) How do we check for occupancy detection?
(pause: 0.8)

## Slide 18: Testing the BSD Card
Run Node Card self-test
Node Bus + DCC power supply power
ESP32 boots
Occupied test with small load
Short test with safe momentary short
I2C reports to Node Card
Events visible in serial output
Notes: (voice: Harrison) Use a small load — something like a resistor wheelset or a 10 k resistor. Touch it across one block’s feeder terminals. If the sensing path and firmware are working, the Occupied LED for that block will light. That confirms the sensor, the firmware thresholds, and the LED logic.
(pause: 0.8)
(voice: Nelson) And how do we test short detection?
(pause: 0.8)
(voice: Harrison) Very briefly create a safe short on the block — just a tap. You should see the Short LED come on immediately. The firmware will shut off that block, wait for its short-recovery delay, and then turn it back on. Seeing the LED behavior and the block power cycling confirms the short-protection logic is running correctly.
(pause: 0.8)
(voice: Nelson) So we’re testing both the sensing and the protection at the same time.
(pause: 0.8)
(voice: Harrison) Exactly. Occupancy tests the lower threshold, short tests the upper threshold, and short recovery tests the solid-state power switch control.
(pause: 0.8)
(voice: Nelson) How do we make sure the Node Card is actually receiving the state updates?
(pause: 0.8)
(voice: Harrison) Open the Node Card’s serial output using WebSerial, Bluetooth, or USB. Every time a block changes state, the BSD Card sends an I2C command to the Node Card. You’ll see messages like “Block 2 Occupied” or “Block 3 Shorted” appear in real time. If the serial output matches the LEDs, the reporting path is working perfectly.
(pause: 0.8)
(voice: Nelson) So a proper test checks four things: the card is detected, the sensors respond, the protection works, and the Node Card receives every change.
(pause: 0.8)
(voice: Harrison) Exactly. If all four pass, the BSD Card is ready to install.

## Slide 19: Troubleshooting
Not detected → I2C address or EEPROM
No LEDs → power issue
Stuck occupied → sensing path
Stuck short → protection circuitry
One dead block → trace that channel
No updates → I2C reporting path
Notes: (voice: Nelson) What are the most common problems someone might see when testing or installing the BSD Card?
(pause: 0.8)
(voice: Harrison) Most issues fall into just a few categories, and the symptoms tell you exactly where to look. The first is when the Node Card doesn’t see the BSD Card during the self-test. If that happens, it’s almost always the I2C address switch being set incorrectly or the EEPROM not being soldered or oriented right. If the EEPROM can’t be read, the Node Card won’t recognize the board.
(pause: 0.8)
(voice: Nelson) So if the card isn’t detected, the problem is almost always addressing or the EEPROM.
(pause: 0.8)
(voice: Harrison) Exactly. The next issue is when none of the LEDs light, even during a short test. That means the BSD Card isn’t receiving the power it expects. You need both the Node Bus logic power and the DCC power supply power for the block stages to work. If either one is missing, the LEDs won’t tell you anything.
(pause: 0.8)
(voice: Nelson) So no LEDs means a power issue — not a sensing issue.
(pause: 0.8)
(voice: Harrison) Right. Then we get into the “per-block” problems. If a block’s Occupied LED is stuck on, even with nothing connected, that means the firmware is seeing current that shouldn’t be there. That usually points to a solder bridge, a component orientation issue, or a wrong-value component in that block’s sensing path.
(pause: 0.8)
(voice: Nelson) And what about a Short LED that’s stuck on?
(pause: 0.8)

## Slide 20: Troubleshooting
Not detected → I2C address or EEPROM
No LEDs → power issue
Stuck occupied → sensing path
Stuck short → protection circuitry
One dead block → trace that channel
No updates → I2C reporting path
Notes: (voice: Harrison) A stuck Short LED means the firmware thinks the block is well above the short threshold. That can be caused by a mis-soldered sensor, a bad connection in the protection components, or a component installed in the wrong orientation. The key is that the behavior is isolated — only that one block is affected.
(pause: 0.8)
(voice: Nelson) So when only one block misbehaves, it’s almost always that block’s individual components.
(pause: 0.8)
(voice: Harrison) Exactly. The BSD Card is very modular — each block is its own subsystem. So a problem on Block 3 won’t affect Block 4. If one block doesn’t respond at all, that’s often a cold solder joint or missing part somewhere in that block’s solid-state power switch, sensor, or input path.
(pause: 0.8)
(voice: Nelson) And what if everything looks good on the card, but the Node Card isn’t showing any updates?
(pause: 0.8)
(voice: Harrison) Then you’re looking at an I2C reporting issue. The BSD Card might be detecting changes correctly, but if the Node Card doesn’t receive the I2C text commands, nothing downstream will update. That’s usually a wiring issue on the Node Bus or an I2C address mismatch.
(pause: 0.8)
(voice: Nelson) So troubleshooting the BSD Card is really just following the layers: first see if the Node Card detects it, then check power, then test each block’s subsystem, and finally confirm the I2C reporting path.
(pause: 0.8)
(voice: Harrison) Exactly. Those four layers — detection, power, per-block behavior, and reporting — isolate every possible issue. Once you walk that sequence, it’s very easy to pinpoint the problem, fix it, and get the card working.

## Slide 21: Integration with Fusion Logic
BSD → Node Card via I2C
Node Card publishes LCC events
Logic rules react instantly
Signals and routes adjust
Short events trigger alerts or voice
Notes: (voice: Nelson)
How does this fit into layout automation? What does the BSD Card actually enable once everything is connected?
(pause: 0.8)
(voice: Harrison) The flow is simple and powerful. The BSD Card decides the block state — clear, occupied, or short — and sends that state to the Node Card through I2C. The Node Card takes that information and publishes the corresponding events to the system.
(pause: 0.8)
(voice: Nelson) And then the automation reacts to those events?
(pause: 0.8)
(voice: Harrison) Exactly. Fusion’s logic engine watches for those events. When a block becomes occupied, the logic can immediately set the signal behind the train to red, lock a turnout, or reserve a route. When a block clears, it can release that route and let the next train move.
(pause: 0.8)
(voice: Nelson) What about shorts? That seems even more important.
(pause: 0.8)
(voice: Harrison) Right — short events are a big deal operationally. When the BSD Card reports a short, the Node Card publishes a short event for that specific block. Logic can announce it, flash an indicator, pause automated movement, or alert the dispatcher. Operators instantly know which block has the problem — not just that “something tripped.”
(pause: 0.8)
(voice: Nelson)
So instead of a whole district going down, you get a targeted alert that fits right into the automation.
(pause: 0.8)

## Slide 22: Integration with Fusion Logic
BSD → Node Card via I2C
Node Card publishes LCC events
Logic rules react instantly
Signals and routes adjust
Short events trigger alerts or voice
Notes: (voice: Harrison) Exactly. Signals drop to stop, routes freeze, audio or voice messages play — all because the BSD Card provided precise, per-block information. It keeps trains safe and prevents cascading problems.
(pause: 0.8)
(voice: Nelson) And the automation rules stay clean because the BSD Card is already giving the system the interpreted block state.
(pause: 0.8)
(voice: Harrison) Right. The logic engine doesn’t have to guess or filter raw signals. It gets well-defined events from the Node Card, driven by BSD state changes. That keeps everything predictable, reliable, and easy to configure in the Admin View.
(pause: 0.8)
(voice: Nelson) So the BSD Card gives the system the high-quality information it needs, and the logic engine turns that information into safe, reliable train movement.
(pause: 0.8)
(voice: Harrison) Exactly. The BSD Card handles the electrical reality, and the automation handles the operational reality. Together, that’s what makes Fusion layouts run smoothly.

## Slide 23: BSD Card Configuration Admin View
Set communication info (Node + BSD address)
Configure occupancy current range
Turnouts: defaults usually fine
Signals: choose PWM Card, lamp lines, aspect setup
Default event IDs work for most setups
Logic: define conditions → choose actions
Notes: (voice: Nelson) Before we wrap up, let’s talk about configuration. What does someone actually need to set up in the Admin View for the BSD Card and the rest of their layout?
(pause: 0.8)
(voice: Harrison) For the BSD Card, the most important setting is the occupancy current range. That range tells the firmware how much current should indicate a train is present. Different locomotives draw different amounts, so it’s adjustable.
(pause: 0.8)
(voice: Nelson) And the card also handles short detection automatically, right?
(pause: 0.8)
(voice: Harrison) Right. Short detection doesn’t require user configuration — the firmware handles that internally. You just set the occupancy range, and you’re done with BSD-specific settings.
(pause: 0.8)
(voice: Nelson) What about turnouts? Any special configuration there?
(pause: 0.8)
(voice: Harrison) For turnouts, the defaults work almost every time. The turnout cards already have built-in event IDs and standard behavior, so most users don’t need to change anything unless they’re doing something unusual.
(pause: 0.8)
(voice: Nelson) Signals are usually more involved. How does that work in Admin View?
(pause: 0.8)

## Slide 24: BSD Card Configuration Admin View
Set communication info (Node + BSD address)
Configure occupancy current range
Turnouts: defaults usually fine
Signals: choose PWM Card, lamp lines, aspect setup
Default event IDs work for most setups
Logic: define conditions → choose actions
Notes: (voice: Harrison) Signals use the PWM Card, and that’s where you choose which PWM Card you’re using, which lines each lamp is connected to, and what aspects the signal supports. The admin uses a CDI Configuration Tool which walks you through selecting the PWM lines for red, yellow, green, or any special lamps. Then you define how those lamps combine to create each aspect.
(pause: 0.8)
(voice: Nelson) And the event values — do people have to manually create all those?
(pause: 0.8)
(voice: Harrison) No. Fusion assigns default event IDs for everything — BSD blocks, turnouts, signals, logic rules — and those work perfectly well for most layouts. Users only customize event IDs if they want to integrate with external LCC devices.
(pause: 0.8)
(voice: Nelson) And logic? Where does that fit in?
(pause: 0.8)
(voice: Harrison) Logic is where you define conditions and actions. A condition might be “Block 2 is occupied” or “Block 3 is shorted,” and the action could be “Set the signal to red” or “Disable a turnout.” It’s all menu-driven in the Admin View, and the logic uses the event IDs you’ve already configured.
(pause: 0.8)
(voice: Nelson) So configuration for Fusion is really a guided process: Set the BSD occupancy range, confirm turnout defaults, define signal lamps and aspects, keep the default events, and then build the logic rules that tie everything together.
(pause: 0.8)
(voice: Harrison) Exactly. And once you do that, the entire system responds instantly to every block change — including shorts — thanks to the Node Card publishing LCC events.

## Slide 25: Fusion & NMRA LCC Foundation
How Fusion Builds on NMRA Standards
Built on the NMRA LCC (Layout Command Control) standard
Uses the open-source OpenLCB / LCC software stack
Fully interoperable with other LCC-compliant products and tools
Extends LCC with modular cards, logic, and DIY-friendly hardware
Credit to NMRA LCC and OpenLCB contributors for the core architecture
Notes: (voice: Nelson) Before we wrap up, it’s worth mentioning the foundation that Fusion is built on. We’re not inventing a new messaging system here — Fusion stands on top of something that already exists in the hobby.
(pause: 0.9)
(voice: Harrison) Exactly. Fusion is built directly on the NMRA’s LCC standard, Layout Command Control. All of the messaging, event handling, and configuration structures follow the same open specifications published by the NMRA.
(pause: 0.9)
(voice: Harrison) And underneath that is the OpenLCB open-source software, developed by a community of volunteers for more than a decade. Fusion uses that stack for everything — the event model, the kanbus messaging, the CDI system — it’s all LCC under the hood.
(pause: 1.1)
(voice: Nelson) And that means it works with other LCC systems, right?
(pause: 0.6)
(voice: Harrison) Exactly. Because Fusion is LCC-compliant, it’s fully interoperable with other LCC-based products — JMRI, signal controllers, button boards, throttles, sensors, configuration tools — anything that speaks LCC will work right alongside Fusion. You can mix and match hardware from different vendors and the system still behaves consistently.
(pause: 1.0)
(voice: Harrison) Fusion simply extends that foundation with modular hardware and DIY-friendly design. But the credit for the underlying architecture belongs to the NMRA LCC team and the OpenLCB developers who maintain the standards and the software that make this level of interoperability possible.

## Slide 26: Wrap-Up
BSD monitors 4 blocks
Occupied + short detection
Auto-reset on short
Sends states via I2C
Node Card publishes events
Notes: (voice: Nelson) Before we finish, let’s talk about the bigger picture. Not just what the BSD Card does — but how it fits into reliability, troubleshooting, and keeping the layout running. Why is this card so important?
(pause: 0.8)
(voice: Harrison) The BSD Card is the first line of defense for the most important blocks on the layout. It monitors four blocks individually, detects occupancy, and instantly reacts to shorts. But what makes it really powerful is how much it simplifies troubleshooting when something goes wrong.
(pause: 0.8)
(voice: Nelson) Right — the troubleshooting slide covered a lot. How does the BSD actually help diagnose problems?
(pause: 0.8)
(voice: Harrison) Look at what the BSD gives you:
The Node Card self-test confirms the card is detected, the address is correct, and the EEPROM is responding.
The LEDs for each block show live occupancy and short states.
If a block stays occupied or shorted, you can trace that exact channel top-to-bottom.
If the Node Card isn’t updating, you know it’s an I2C reporting issue, not a block issue.
If no LEDs work at all, you know it’s a power issue — Node Bus or DCC power supply.
All of those align directly with the troubleshooting bullets, and all of them cut down debugging time dramatically.
(pause: 0.8)
(voice: Nelson) So the BSD Card isn’t just protecting four blocks — it’s helping the user see exactly where a problem is.
(pause: 0.8)
(voice: Harrison) Exactly. Traditional layouts hide electrical issues. A DCC power supply trips and you have no idea which block caused it. With Fusion and the BSD Card, the system tells you which block, why, and what state it’s in. You get clear, occupied, short — and even short-recovery behavior — right on the LEDs and right in the Node Card’s serial output.
(pause: 0.8)
(voice: Nelson) And because the BSD handles short protection locally, the rest of the layout keeps running.
(pause: 0.8)

## Slide 27: Wrap-Up
BSD monitors 4 blocks
Occupied + short detection
Auto-reset on short
Sends states via I2C
Node Card publishes events
Notes: (voice: Harrison) Right. A short on Block 3 doesn’t bring down the whole district. The BSD isolates the problem, resets it, and reports it. That distributed protection is the reason Fusion uses edge computing — each card handles its own job so failures stay local.
(pause: 0.8)
(voice: Nelson) And that ties straight into the troubleshooting logic — you always know whether the issue is the card, the block channel, the Node Bus, or I2C reporting.
(pause: 0.8)
(voice: Harrison) Exactly. Troubleshooting becomes layered and predictable, not guesswork. The BSD Card was designed from the ground up so builders, operators, and dispatchers can quickly pinpoint issues and keep trains moving.
(pause: 0.8)
(voice: Nelson) So in the end, the BSD Card is: a detector, a protector, a diagnostic tool, and a clean integration point into Fusion’s logic and LCC events.
(pause: 0.8)
(voice: Harrison) Right. It’s not just about sensing current — it’s about delivering reliable operations, faster troubleshooting, and a safer layout. That’s why the BSD Card is such a critical part of the Fusion architecture.