## Slide 1: Quantitative PRoteomics
Systems Medicine Course – February 19th 2020
Fredrik Edfors, PhD
Science for Life Laboratory, Stockholm, Sweden

## Slide 2: Lecture outline
Introduction
    Mass spectrometry – The basics you need to know
    Bottom-up proteomics
Quantitative Proteomics
    Data Independent Acquisition (DIA)
    Targeted proteomics
    Precision medicine applications
Workshop – From raw data to quantified protein
    Quantitative accuracy and precision
    Data Independent Acquisition (DIA)
    Selective Reaction Monitoring (SRM)

## Slide 3: Proteomics
Proteome
  The complement protein found in a single cell in a particular environment
  Complete collection of proteins encoded by the genome of an organism
Proteomics
  The study of composition, structure, function and interaction of the proteins directing the activities of each living cell
Definitions

## Slide 4: Intended learning outcomes
Describe the key technical challenges in a proteomics analysis
Perform analysis and filter out your proteins of interest from raw proteomics data (DIA)
Perform differential expression analysis, principal component analysis and clustering of data
Notes: (functional GO and KEGG pathway analysis)

## Slide 5: Why do we need Proteomics
Comprehensive datasets can easily be generated using transcriptomics
Selective pressure is acting at the protein-level
  The level of transcription is not a quantitative estimate of its corresponding protein level -> Translation efficiency
When absolute quantification is needed
Achieved by either sensitive antibody-based assays or specific LC-MS/MS
Motivation
Absolute and
Relative Abundance
Turnover
PTM analysis
Protein Isoforms
Complexes and Protein Protein Interactions
Localization

## Slide 6: Benefits of Mass spectrometry
No affinity reagent needed
High precision
Good linear range
Good sensitivity
High multiplexing capability
Drawbacks
  Expensive instrumentation
  Low throughput

## Slide 7: Understanding a Mass spectra
Notes: Mass-to-charge
Monoisotopic mass
Predictable
Accurate measurements,

## Slide 8: OVerview
Sample Preparation
LC-MS/MS
Detectors
Orbitrap
Triple quadrupole
Time-of-flight (TOF)
Monoisotopic mass
Mass of the most abundant isotope of a molecule
Measured in amu or Da
Notes: Most elements have more than one stable isotope.
For example, most carbon atoms have a mass of 12 Da, but in nature, 1.1% of C atoms have an extra neutron, making their mass 13 Da.
Why do we care?
Mass spectrometers “see” the isotope peaks provided the resolution is high enough.
If an MS instrument has resolution high enough to resolve these isotopes, better mass accuracy is achieved.

## Slide 9: Proteomics
Bottom-down
  Analyzing proteins
Bottom-up
  Analyzing peptides
Figure: https://en.wikipedia.org/wiki/Bottom-up_proteomics

## Slide 10: Analyzing Peptides
Protein extraction followed by digestion
Enzymatic degradation
  Trypsin most commonly used enzyme
  Cleaves after R or K
Proteomics beyond trypsin, Liana Tsiatsiani, Albert J. R. Heck

## Slide 11: Peptide Fragmentation
Example: Targeted measurement of one peptide
Quantified Peptide

## Slide 12
Real world
example

## Slide 13: Identifying peptides
A survey of computational methods and error rate estimation procedures for peptide and protein identification in shotgun proteomics
Alexey I. Nesvizhskii

## Slide 14: Database search
A survey of computational methods and error rate estimation procedures for peptide and protein identification in shotgun proteomics
Alexey I. Nesvizhskii

## Slide 15: Parsimony
Remember
  We are not doing protein quantitation
  We are doing peptide quantitation
  Re-assembling proteins from peptide sequences
Building Proteins From Peptides
Notes: Solution, use other enzymes

## Slide 16: Controlling The False discovery Rate
A number of reasons can cause a PSM to be false, these include:
  Low quality spectrum
  Peptides not in the database
  Imperfect scoring function
Target Decoy Model
A survey of computational methods and error rate estimation procedures for peptide and protein identification in shotgun proteomics
Alexey I. Nesvizhskii
Notes: Solution, use other enzymes
..Now when we know how to identify proteins.

## Slide 17: Label free Quantification
Spectral counting
  Number of MS/MS events
Intensity-based
  Peak integration
  Precursor signal intensity
  Reporter ion signal intensity
Comparative and Quantitative Global Proteomics Approaches: An Overview

## Slide 18: Ion intensity
Assumption
  Signal intensity from electrospray ionization (ESI) correlates with ion concentration
  The height or area of a peak at particular m/z reflects the number of ions for that m/z
Abundance cannot be used to directly infer absolute protein or peptide concentration.

## Slide 19: Label free quantification
Cox J et al Accurate proteome-wide label-free quantification by delayed normalization and maximal peptide ratio
extraction, termed MaxLFQ. Mol Cell Proteomics. American Society for Biochemistry and Molecular Biology; 2014 Sep;13(9):2513–26.
Spectral Counting
Summed Intensities
Label Free Quant
  IBAQ
    Total intensities divided by the identified peptides for one protein
  MaxLFQ
    Exclude some "outliers" to best represent the ratio changes of different samples
Spectral Count
Summed intensities
MaxLFQ

## Slide 20: Quantitative Proteomics
What type of quantitative accuracy do we need?
  Fold-change?
  Percentage increase/decrease?
Courtesy of MacCoss Lab

## Slide 21: Discovery vs Targeted
Doerr, A. Mass spectrometry–based targeted proteomics. Nat Methods 10, 23 (2013)

## Slide 22: Ion Sampling Strategies
Shotgun Proteomics
Discovery of new peptides Data Dependent Acquisition Limitations Top-(n) peaks selected for MS/MS Different targets identified between runs
Targeted Proteomics
Pre-defined list of peptides Data Independent Acquisition Limitations Cannot discover new peptides/proteins Assay development for every analyte Parameters to consider
    Ionization
    Fragmentation
    Retention Time

## Slide 23: Instrumentation for Targeted Proteomics
SRM
PRM

## Slide 24: Robust Quantification
Benefits of Targeted Proteomics
  Same data is harvested every run
  More consistent data
  Easier to compare between case / control
Drawback
  Peptides has to be well characterized
    Ionization
    Retention time
    Fragmentation
  Assay development
Data Quality

## Slide 25: Standard Curves
  Suitable for for clinical applications
  Convert signal intensity to quantity
Courtesy of MacCoss Lab
Notes: K = slope of the standard curve
Ab = area of blank

## Slide 26: Quantitative proteomics
Picture adapted from: Quantitative mass spectrometry in proteomics: a critical review
Different Strategies
Notes: Antibodies mainly used for IHC, IF in the atlas. Other applications other possible, and if we look at an IHC microscope image..
Marcus Bantscheff

## Slide 27: Spectrum Count ≉ MS intensity
Chart: SRM Signal Intensity
 | 7 | 5 | 2 | 4 | 5 | 4 | 7 | 3 | 2 | 8 | 2 | 7 | 5 | 5 | 1 | 2 | 7 | 7 | 4 | 4 | 6 | 3 | 2 | 2 | 6 | 3 | 1 | 3 | 2 | 1 | 10
Prakash, A. et al. J Proteome Res. 2009 8(6): 2733–2739.
Apolipoprotein B100

## Slide 28: Standard Curves
  Introduce internal standards for robust quantification
Courtesy of MacCoss Lab
Notes: K = the slope of the standard curve
R = area ratio from blank.

## Slide 29: Targeted workflow
Gold-standard for protein quantification
  Standard curve
  Internal standard
Time consuming -> high cost
Limiting the number of possible analytes
Peptide Selection
Chromatogram Extraction
Peak Integration
Transition Refinement
Hypothesis Generation
Hypothesis Test

## Slide 30: DIA workflow
Monitor all tryptic peptides
  Create a digital record of your sample
High responding peptides
  Similar to SRM
Peptides in a spectral library
  Identified by DDA
  Predicted by PROSIT
Peptide Selection
Chromatogram Extraction
Peak Integration
Transition Refinement
Hypothesis Generation
Hypothesis Test

## Slide 31: Data Independent Acquisition
“All” Reaction Monitoring (coined by Bruce Lab)
20 20 m/z-wide windows = 400 m/z
m/z
500
900
Measure all fragment ions for all precursors between 500 and 900 m/z
Orbitrap
Linear Ion Trap
TOF
FT-ICR
Courtesy of MacCoss Lab

## Slide 32: Comprehensive MS/MS Acquisition
20 20 m/z-wide windows = 400 m/z
m/z
500
900
Time
~2 seconds
Precursor Filter
780-800 m/z
Orbitrap Mass Analyzer
Courtesy of MacCoss Lab

## Slide 33: Building a spectral library
Ludvig et al (2018) Data‐independent acquisition‐based SWATH‐MS for quantitative proteomics: a tutorial

## Slide 34: Deconvoluting DIA runs
Nathalie Selevsek et al. Reproducible and Consistent Quantification of the Saccharomyces cerevisiae Proteome by SWATH-mass spectrometry, MCP

## Slide 35
Data Acquisition
Peptide Selection
Chromatogram Extraction
Peak Integration
Transition Refinement
Hypothesis Generation
Hypothesis Test
Data Acquisition
Peptide Selection
Hypothesis Generation
Hypothesis Test
Transition Selection or Refinement
RT Scheduling
Peak Integration
DIA
SRM

## Slide 36
Data Acquisition
Peptide Selection
Chromatogram Extraction
Peak Integration
Transition Refinement
Hypothesis Generation
Hypothesis Test
Data Acquisition
Peptide Selection
Hypothesis Generation
Hypothesis Test
Transition Selection or Refinement
RT Scheduling
Peak Integration
DIA
SRM

## Slide 37
Resource of Recombinant proteins used for Antibody generation
Notes: Need for reagents. Generate at least two verified antibodies towards every human protein.
Large scale setup for the systematic analysis of all human proteins by affinity based methods.

## Slide 38
Pipeline for Targeted proteomics Assay generation
And PEPTIDE
Quantification
Notes: Basically 5 years of graudate studies summarized in one workflow-slide.
Proteotypic peptide
  Good ionization
  No miscleavages
  No methionine
  Unique to one single human gene

## Slide 39
Selecting the best peptides for protein quantification
Notes: Bioinformatics evaluation revealed that the resource can cover over 15,000 human genes with at least two unique proteotypic peptides
14,000 of 19,000 PrESTs were experimentally verified proteotypic peptide.
In total 10,163 unique human proteins covered by at least one proteotypic peptide.

## Slide 40: Toolbox for proteomics
Human Protein Atlas Resource
Antigens
Recombinant protein fragments produced in Escherichia coli
>50,000 proteins passed QC for assay generation
Antibodies
Affinity purified polyclonal Ab’s
>25,000 Ab’s passed QC
Available from Atlas Antibodies
Notes: How to utilize the resource.
Antibodies mainly used for IHC, IF and published onto the atlas.
Other applications other possible, and if we look at an IHC microscope image..
So if we have a closer look at the recombinant proteins used for immunization..

## Slide 41: Recombinant Protein fragments
PrESTs from HPA
Zeiler M, Straube WL, Lundberg E, Uhlén M, Mann M (2012) MCP

## Slide 42: Full-length vs Protein Fragment
Peptide coverage

## Slide 43: Full-length vs Protein Fragment
Peptide coverage

## Slide 44: Full-length vs Protein Fragment
Peptide coverage

## Slide 45
Oeckl P, Steinacker P, Otto M. Comparison of Internal Standard Approaches for SRM Analysis of Alpha-Synuclein in Cerebrospinal Fluid. J Proteome Res. American Chemical Society; 2017 Nov 14;17(1):516–23.
Peptide
performance

## Slide 46: What peptide shall we use?
Edfors et al.
Heavy
Light
MPLLLLLPLLWAGALAMAAAEVSADQVATVMWDYFSQLSNNAKEAVEHLQKSELTQQLNALFQDKLGEVNTYAGDLQKKLVPFATELHERLAKDSEKLKEEIGKELEELRARLLPHANEVSQKIGDNLRELQQRLEPYADQLRTQVNTQAEQLRRQLTPYAQRMERVLRENADSLQASLRPHADELKAKIDQNVEELKGRLTPYADEFKVKIDQTVEELRRSLAPYAQDTQEKLNHQLEGLTFQMKKNAEELKARISASAEELRQRLAPLAEDVRGNLRGNTEGLQKSLAELGGHLDQQVEEFRRRVEPYGENFNKALVQQMEQLRQKLGPHAGDVEGHLSFLEKDLRDKVNSFFSTFKEKESQDKTLSLPELEQQQEQQQEQQQEQVQMLAPLESGAPENLYFQGEDQVDPRLIDGK
APOA4
1. Measure
2. Combine
3. Sequence coverage
Light
Heavy

## Slide 47: Selecting the optimal peptide

## Slide 48: PEPTIDE formation Kinetics
Trypsin Digestion
QPrEST standards
5
15
30
360
60
Trypsin Digestion
…

## Slide 49: Apolipoproteins
Associated with transport of different sizes of lipid droplets
  Only APOB and APOA1 are monitored in clinics today
  What about the rest?
Application
APOB
APOA1
APOE
APOH
APOA4
APOB
APOE
APOM
APOH
VLDL
Chylomicron
HDL
LDL
PreB-HDL
APOA1
APOA1
APOA2
APOL1
APOC
APOD
APOE
APOM
APOJ (CLU)
APOB
APOM
APOH
APOD
Picture adopted from MabTech
Hober et al. Absolute Quantification of Apolipoproteins Following Treatment with Omega-3 Carboxylic Acids and Fenofibrate Using a High Precision SIS PrEST -Based SRM, In review
Notes: 20 pmol per ul down to 50fmol
Epanova (FDA approved omega 3 fatty acid)
Fenofibrate (reduce cholesterol)= Reduces LDL and VLDL

## Slide 50: SRM assay generation
Goal: Enable quantification of 14 apolipoproteins in human plasma using SRM.
34 peptides in 25 minutes
Proteins covered by QPrESTs
Notes: 20 pmol per ul down to 50fmol

## Slide 51: Peptide Selection Process

## Slide 52: Serial dilution in plasma
Reverse Standard Curves

## Slide 53: Define Linear Range
APOM
APOE

## Slide 54: Performance over time
3-by-5 technical evaluation
  One plasma sample processed over 5 days
14 proteins

## Slide 55
Accuracy and Precision of SIL Standards spiked to human plasma

## Slide 56: Effect 1 - Study outline
Clinical Analysis
FDA approved Omega-3 fatty acid
TRICOR
Notes: Current guidelines advocate the use of marine-derived omega-3 fatty acids
supplements for the prevention of coronary heart disease and major vascular events in
people with prior coronary heart disease, but large trials of omega-3 fatty acids have
produced conflicting results.
Several large trials have reported conflicting results of the associations of supplementation with omega-3 FA
EPANOVA is indicated as an adjunct to diet to reduce triglyceride (TG) levels in adult patients with severe (≥500 mg/dL) hypertriglyceridemia.
Fenofibrate has been used since 1975 and is one of the most commonly prescribed fibrates
It is mainly used to reduce cholesterol levels in people at risk of cardiovascular disease. Like other fibrates, it reduces both low-density lipoprotein (LDL) and very low density lipoprotein (VLDL) levels, as well as increasing high-density lipoprotein (HDL) levels and reducing triglyceride levels, It is used alone or along with statins in the treatment of hypercholesterolemia and hypertriglyceridemia.

## Slide 57: Quantify Change from Base-Line
Notes: Current guidelines advocate the use of marine-derived omega-3 fatty acids
supplements for the prevention of coronary heart disease and major vascular events in
people with prior coronary heart disease, but large trials of omega-3 fatty acids have
produced conflicting results.
Several large trials have reported conflicting results of the associations of supplementation with omega-3 FA
EPANOVA is indicated as an adjunct to diet to reduce triglyceride (TG) levels in adult patients with severe (≥500 mg/dL) hypertriglyceridemia.
Fenofibrate has been used since 1975 and is one of the most commonly prescribed fibrates
It is mainly used to reduce cholesterol levels in people at risk of cardiovascular disease. Like other fibrates, it reduces both low-density lipoprotein (LDL) and very low density lipoprotein (VLDL) levels, as well as increasing high-density lipoprotein (HDL) levels and reducing triglyceride levels, It is used alone or along with statins in the treatment of hypercholesterolemia and hypertriglyceridemia.

## Slide 58: Results
Hober et al. (2019) Absolute Quantification of Apolipoproteins Following Treatment with Omega-3 Carboxylic Acids and Fenofibrate Using a High Precision SIS PrEST -Based SRM, MCP

## Slide 59: Summary
  Immunoassays are an imperfect solution to the protein quantitation problem
  Add the internal standard as early as possible to account for sample preparation errors
  Think about what type of quantification accuracy/precision you need
  13C labeled internal standards aren’t perfect, but the best alternative

## Slide 60: Workshop after the break
Work with one DIA dataset
Human plasma
  Individuals from two groups
  QC samples
Peptide quantification
  Differential expression analysis
Validation using internal standards (SRM)

## Slide 61: Acknowledgements
Mathias Uhlén
Andreas Hober
David Kotol
Björn Forsström
Linn Fagerberg
Scilifelab
Tasso Miliotis
Astra Zeneca
Anne-Sophie Svensson
Anna Berling
Hanna Tegel
Sophia Hober
Protein production
The Skyline Team
Notes: s